## Slide 1: On Demand Paging (ODP) Update
Liran Liss
Mellanox Technologies

## Slide 2: Agenda
Introduction
Implementation notes
APIs and usage
Statistics
What’s new

## Slide 3: Memory Registration Challenges
Registered memory size limited to physical memory
Requires special memory locking privileges
Registration is a costly operation
Requires careful application design for high performance
  Bounce buffers
  Pin-down caches
Keeping address space and registered memory in synch is hard and error prone

## Slide 4: On Demand Paging
MR pages are never pinned by the OS
  Paged in when HCA needs them
  Paged out when reclaimed by the OS
HCA translation tables may contain non-present pages
  Initially, a new MR is created with non-present pages
  Virtual memory mappings don’t necessarily exist
Advantages
  Greatly simplified programming
    Reduce/eliminate registrations, no copying, no caches
  Unlimited MR sizes
    No need for special privileges
  Physical memory optimized to hold current working set
    For both CPU and IO access

## Slide 5: ODP Operation
0x1000
PFN1
0x2000
PFN2
0x3000
PFN3
0x4000
PFN4
0x5000
PFN5
0x6000
PFN6
0x1000
0x2000
0x3000
0x4000
0x5000
0x6000
Address Space
IO Virtual Address
HCA data
access
OS PTE change
Page fault!
ODP promise:
IO virtual address mapping == Process virtual address mapping

## Slide 6: Implementation
ib_core
mlx5_core/
mlx5_ib
Key->MR tree
MR interval tree
HCA
MR
umem
mlx5_ib_mr
Page/DMA list
HW translation tables
Kernel
QP page fault event
mmu_notifer page invalidation

## Slide 7: ODP capabilities
enum odp_transport_cap_bits {
ODP_SUPPORT_SEND = 1 << 0,
ODP_SUPPORT_RECV = 1 << 1,
ODP_SUPPORT_WRITE = 1 << 2,
ODP_SUPPORT_READ = 1 << 3,
ODP_SUPPORT_ATOMIC = 1 << 4,
};
enum odp_general_caps {
ODP_SUPPORT = 1 << 0,
};
struct ibv_odp_caps {
uint32_t comp_mask;
uint32_t general_caps;
struct {
uint32_t rc_odp_caps;
uint32_t uc_odp_caps;
uint32_t ud_odp_caps;
uint32_t xrc_odp_caps;
} per_transport_caps;
};
int ibv_query_odp_caps(struct ibv_context *context,
struct ibv_odp_caps *caps,
size_t caps_size);

## Slide 8: ODP Memory Regions
Registering the whole address space
  ibv_reg_mr(pd, NULL, (u64) -1, flags)
  Memory windows may be used to provide granular remote access rights
enum ibv_access_flags {
IBV_ACCESS_LOCAL_WRITE = 1,
IBV_ACCESS_REMOTE_WRITE = (1<<1),
IBV_ACCESS_REMOTE_READ = (1<<2),
IBV_ACCESS_REMOTE_ATOMIC = (1<<3),
IBV_ACCESS_MW_BIND = (1<<4),
IBV_ACCESS_ON_DEMAND = (1<<5)
};
struct ibv_mr *ibv_reg_mr(struct ibv_pd *pd, void *addr,
size_t length, int access);

## Slide 9: Usage Example
int main()
{
struct ibv_odp_caps caps;
ibv_mr *mr;
struct ibv_sge sge;
struct ibv_send_wr wr;
...
if (ibv_query_odp_caps(ctx, &caps, sizeof(caps)) ||
!(caps.ud_odp_caps & ODP_SUPPORT_SEND))
return -1;
...
p = mmap(NULL, 10 * MB, PROT_READ | PROT_WRITE, MAP_SHARED, 0, 0);
...
mr = ibv_reg_mr(ctx->pd, p, 10 * MB, IBV_ACCESS_LOCAL_WRITE | IBV_ACCESS_ON_DEMAND);
...
sge.addr = p;
sge.lkey = mr->lkey;
ibv_post_send(ctx->qp, &wr, &bad_wr);
...
munmap(p, 1 * MB);
p = mmap(p, 1 * MB, PROT_READ | PROT_WRITE, MAP_SHARED, 0, 0);
...
ibv_post_send(ctx->qp, &wr, &bad_wr);
...
return 0;
}

## Slide 10: Memory Prefetching
Best effort hint
  Not necessarily all pages are pre-fetched
  No guarantees that pages remain resident
  Asynchronous
    Can be invoked opportunistically in parallel to IO
Use cases
  Avoid multiple page faults by small transactions
  Pre-fault a large region about to be accessed by IO
EFAULT returned when
  Range exceeds the MR
  Requested pages not part of address space
struct ibv_prefetch_attr {
uint32_t comp_mask;
int flags; /* IBV_ACCESS_LOCAL_WRITE */
void *addr;
size_t length;
};
int ibv_prefetch_mr(struct ibv_mr *mr,
struct ibv_prefetch_attr *attr,
size_t attr_size);

## Slide 11: Statistics
Core statistics
  Maintained by the IB core layer
  Tracked on a per device basis
  Reported by sysfs
Use cases
  Page fault pattern
    Warm-up
    Steady state
  Paging efficiency
  Detect thrashing
  Measure pre-fetch impact
/sys/class/infiniband_verbs/uverbs<dev-idx>/
invalidations_faults_contentions
num_invalidation_pages
num_invalidations
num_page_fault_pages
num_page_faults
num_prefetches_handled
Counter name | Description
invalidations_faults_contentions | Number of times that page fault events were dropped or prefetch operations were restarted due to OS page invalidations
num_invalidation_pages | Total number of pages invalidated during all invalidation events
num_invalidations | Number of invalidation events
num_page_fault_pages | Total number of pages faulted in by page fault events
num_page_faults | Number of page fault events
num_prefetches_handled | Number of prefetch Verb calls that completed successfully

## Slide 12: Statistics (continued)
Driver debug statistics
  Maintained by the mlx5 driver
  Tracked on a per device basis
  Reported by debugfs
Use cases
  Track accesses to non-mapped memory
  ODP MR usage
/sys/kernel/debug/mlx5/<pci-dev-id>/odp_stats/
num_failed_resolutions
num_mrs_not_found
num_odp_mr_pages
num_odp_mrs
Counter name | Description
num_failed_resolutions | Number of failed page faults that could not be resolved due to non-existing mappings in the OS
num_mrs_not_found | Number of faults that specified a non-existing ODP MR
num_odp_mr_pages | Total size in pages of current ODP MRs
num_odp_mrs | Number of current ODP MRs

## Slide 13: News
Connect-IB Support
  Initially UD and RC
    DC will follow
  Address space key for local access
Initial testing with OpenMPI
  No more memory hooks!
Release planned for MLNX_OFED-2.3
ODP patches submitted to kernel

## Slide 14: Thank You