## Slide 1
Stan Smith Intel SSG/DPD
June, 2015
Kernel Fabric Interface
KFI Framework

## Slide 2: Background
OpenFabrics Interfaces WG (OFI WG) created by OFA 8/2013
Charter is to develop, test and distribute:
  An extensible, open source framework that provides access to high-performance fabric interfaces and services.
  Extensible, open source interfaces aligned with ULP and application needs for high-performance fabric services
In short, deliver I/O stack(s) that maximize application effectiveness
OFI WG takes an ‘application-centric’ view of the API
  The focus is on the consumers of network services
  Thus, OFI WG is organized in a slightly different way – by ‘classes of applications’
Notes: This is an attempt to explain the 3 categories on the previous slide

## Slide 3: Taxonomy
Created a taxonomy for classes of applications
  helps us focus on defining the reqmts for each class
  launched two working groups to focus on the first two classes
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Msg passing
MPI middleware
Structured data
Unstructured data
Skts apps
IP apps
Shared memory
- PGAS
- languages (SHMEM, UPC…)
OFI WG
DS/DA WG
OpenFabrics Interfaces - OFI

## Slide 4: Context
OpenFabrics Interfaces is the name for sets of APIs and services focused on specific network use cases:
  libfabric: a user-mode library for distributed and parallel computing
  kfabric: kernel modules for storage and data access
  expect future development to focus on user-mode storage
    user filesystems, byte addressable memory, etc.
kfabric provides kernel mode operations only
  kfabric is not the kernel component of libfabric
  libfabric providers access needed kernel services using the provider’s kernel drivers
Notes: This is an attempt to explain the 3 categories on the previous slide

## Slide 5: kfabric Mission
Create network APIs to support kernel-based storage apps
  filesystems, object I/O, block storage
  Incorporate high performance storage interfaces
  Focus on emerging storage technologies e.g. NVM
Transport independence, consumer portability
  Define an API which is not derived from a specific network technology
  Base the API on a higher level abstraction based on message passing semantics
Emphasis on performance and scalability
  Minimize code paths to device functionality for performance
  Focus on optimizing critical code paths
  Eliminate code branches from critical paths wherever possible
Smooth transition path from existing kernel verbs
  future proofs the kernel fabric stack (ibverbs) with a fabric independent framework
Notes: This is an attempt to explain the 3 categories on the previous slide

## Slide 6: KFI Framework
KFI API
KFI API
KFI Providers
Device Drivers
New Providers
New Devices
NIC
Kernel Sockets
Sockets Provider
kernel Verbs
iWarp
InfiniBand
RoCE
Verbs Provider
* Red = new kernel components

## Slide 7: KFI API
KFI interfaces form a cohesive set
and not simply a union of disjoint interfaces.
The interfaces are logically divided into two groups:
control interfaces: operations that provide access to local communication resources.
communication interfaces expose particular models of communication and fabric functionality, such as message queues, remote memory access, and atomic operations. Communication operations are associated with fabric endpoints.
kfi applications typically use control interfaces to discover local capabilities and allocate resources. They then allocate and configure a communication endpoint to send and receive data, or perform other types of data transfers, with storage endpoints.

## Slide 8: KFI API
KFI API exports up
kfi_getinfo() kfi_fabric() kfi_domain() kfi_endpoint() kfi_cq_open() kfi_ep_bind()
kfi_listen() kfi_accept() kfi_connect() kfi_send() kfi_recv() kfi_read() kfi_write()
kfi_cq_read() kfi_cq_sread() kfi_eq_read() kfi_eq_sread() kfi_close() …
KFI API exports down
kfi_provider_register() During kfi provider module load a call to kfi_provider_register() supplies the kfi-api with a dispatch vector for kfi_* calls.
kfi_provider_deregister() During kfi provider module unload/cleanup kfi_provider_deregister() destroys the kfi_* runtime linkage for the specific provider (ref counted).
KFI API (extremely thin code layer)
Notes: Not sure this helps. It’s meant to suggest messages can be used for specific purposes, like at a trade show or as an element of recruiting

## Slide 9: KFI Provider
kfi_provider_register (uint version, struct kfi_provider *provider)
kfi_provider_deregister (struct kfi_provider *provider)
struct kofi_provider {
const char *name;
uint32_t version;
int (*getinfo)(uint32_t version, const char *node,
const int service, uint64_t flags,
struct fi_info *hints, struct kfi_info **info);
int (*freeinfo)(struct kfi_info *info);
int (*fabric)(struct kfi_fabric_attr *attr,
struct fid_fabric **fabric, void *context);
};

## Slide 10
Thank you

## Slide 11
Back-up

## Slide 12: KFI Application Flow
Initialization
Server connection setup (if required)
Client connection setup (if required)
  Connection finalization (if required)
Data transfer
Shutdown

## Slide 13: KFI Initialization
kfi_getinfo( &fi ) Acquire a list of desirable/available fabric providers.
Select appropriate fabric (traverse provider list).
kfi_fabric(fi, &fabric) Create a fabric instance based on fabric provider selection.
kfi_domain(fabric, fi, &domain) create a fabric access domain object.

## Slide 14: KOFI End Point setup
kfi_ep_open( domain, fi, &ep ) create a communications endpoint.
kfi_cq_open( domain, attr, &CQ ) create/open a Completion Queue.
kfi_ep_bind( ep, CQ, send/recv ) bind the CQ to an endpoint
kfi_enable( ep ) Enable end-point operation (e.g. QP->RTS).

## Slide 15: kOFI connection components
kfi_listen() listen for a connection request
kfi_bind() bind fabric address to an endpoint
kfi_accept() accept a connection request
kfi_connect() post an endpoint connection request
kfi_eq_sread() blocking read for connection events.
kfi_eq_error() retrieve connection error information

## Slide 16: KFI Reliable Datagram transfer
kfi_sendto() post a Reliable Datagram send request
kfi_recvfrom() post a Reliable Datagram receive request.
kfi_cq_sread() synchronous/blocking read CQ event(s).
kfi_cq_read() non-blocking read CQ event(s).
kfi_cq_error() retrieve data transfer error information
fi_close() close any kofi created object.

## Slide 17: KFI message data transfer
  kfi_mr_reg( domain, &mr ) register a memory region
  kfi_close( mr ) release a registered memory region
  kfi_send( ep, buf, len, fi_mr_desc(mr), ctx ) post async send from memory request.
  kfi_recv( ep, buf, len, fi_mr_desc(mr), ctx ) post async read into memory request.
  kfi_sendmsg() post send using fi_msg (kvec + imm data).
  kfi_readmsg() post read using fi_msg (kvec + imm data).

## Slide 18: KFI RDMA data transfer
kfi_write() post RDMA write.
kfi_read() post RDMA read.
kfi_writemsg() post RDMA write msg (kvec).
kfi_readmsg() post RDMA read msg (kvec).

## Slide 19: KFI message data transfer
kfi_send() post send.
kfi_recv() post read.
kfi_sendmsg() post write msg (kvec + imData).
kfi_recvmsg() post read msg (kvec+ imData).
kfi_recvv(), kfi_sendv() post recv/send with kvec.

## Slide 20: Bonepile
To be deleted prior to use

## Slide 21: Kfabric Mission
Future proof the kernel fabric stack (ibverbs) with a fabric independent framework.
Migrate fabric I/F from device specific to higher level message passing semantics.
Streamline code paths to device functionality (reduced instruction counts).
Incorporate high performance storage interfaces.
Coexist with current Verbs interfaces.
Notes: This is an attempt to explain the 3 categories on the previous slide