## Slide 1: IB Verbs Compatibility
Sean Hefty
Intel Corporation

## Slide 2: (Scalable) Fabric Interfaces
Q: What is implied by incorporating interface sets under a single framework?
  Objects exist that are usable between the interfaces
    Isolated interfaces turn the framework into a complex dlopen
  Interfaces are composable
    May be used together
Fabric Interfaces
Message Queue
Control
Interface
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services
Cohesive interfaces, not merely a union

## Slide 3: Verbs Compatibility
Verbs API and data structures supportable through a compatibility mode
  Verbs objects may be converted to FI objects
    ibv_qp  fid_ep, ibv_cq  fid_ec
  FI objects do not necessarily convert to verbs
Provide access to native FI objects
  Expose fields through ibverbs data structures
  Allows use of FI APIs
Applications migrate to FI to use new features

## Slide 4: Migrating Providers from Verbs to FI
libfabric
CM Services
libibverbs
FI
RDMA CM
Verbs Provider
Message Queue
RDMA
Verbs
Verbs Provider
ibverbs abstraction layer
Providers can integrate into framework with minimal changes
Providers leverage abstraction layer and RDMA CM capabilities
Add optimize data transfers and completion processing calls to avoid translation overhead

## Slide 5: Migrating Apps from Verbs to FI
Expose ‘verbs’ interfaces directly from FI
Use macros or static inline functions to convert ‘libibverbs’ exported calls to FI calls
  Same performance as using libibverbs directly
Redefine verb data structures
  Expose native FI definitions
FID
Socket
Reliable datagram message
Message queue
Event collector
Completion queue
CM events
Address vector
Maps
Tables
Interface
uverbs
ucma
Domain
Shared resources
Counter
Memory descriptor
ibverbs
www.openfabrics.org
Goal is to support apps with only recompiling

## Slide 6: Verbs Compatibility
Define fi_ops_ibv
  Includes prototypes for libibverbs APIs
ibv_get_device_list() – inline call
  First call made by any app
  Maps to fi_open(“ibv_devices” …)
Redefine struct ibv_* for use with libfabric
  ibv_device, ibv_context, ibv_pd, ibv_mr, ibv_srq, ibv_qp, ibv_cq,ibv_ah, ibv_comp_channel
  Hide internal fields, reference FI objects

## Slide 7: Compatibility
RDMA CM handled in a similar fashion
  More challenging, not a single top-level entry point
Need to determine how to handle header files
  Avoid conflicting with libibverbs and librdmacm headers
  Could require source change to use new header