## Slide 1: OFA Openframework WG
SHMEM/PGAS Developer Community Feedback 2/2014

## Slide 2: This material was assembled with help of the following organizations/people
Los Alamos National Lab
  Latchesar Ionkov
  Ginger Young
Oak Ridge National Lab
  Steve Poole
  Pavel Shamis
Sandia National Lab
  Brian Barrett
Intel
  David Addison
  Charles Archer
  Sayantan Sur
Mellanox
  Liran Liss
Cray
  Monika ten Bruggencate
  Howard Pritchard (scribe)
Input was also obtained from Paul Hargrove (LBL) and Jeff Hammond (ANL), and others.

## Slide 3: Outline
Brief SHMEM and PGAS intro
Feedback from developers concerning API requirements
  Endpoint considerations
  Memory registration
  Remote memory references
  Collectives
  Active messages

## Slide 4: (Open)SHMEM
symmetric heap
PE 0
1
2
NPES - 1
Data segments
Library based one-sided program model
All ranks (PEs) in the job run the same program (SPMD)
Only objects in symmetric regions – data segment(s), symmetric heap – are guaranteed to be remotely accessible
Various vendor specific variations/extensions
Somewhat archaic interface (think Cray T3D), being modernized as part of OpenSHMEM effort
vaddr space

## Slide 5: UPC
Compiler based program model – ‘c’ with extensions
Each thread has affinity to a certain chunk of shared memory
Objects declared as shared are allocated out of shared memory
Objects can be distributed across the chunks of shared memory in various ways – blocked, round robin, etc.
Collective operations, locks, etc.
Like MPI, evolving over time
Thread may map to SHMEM PE rank enumeration
Thread 0
2
THREADS - 1
vaddr space
1
shared address space
private address space
x[T*3]
x[(T*3)+1]
x[(T*3)+2]
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
x[8]
x[(T-1)*3]
x[(T-1)*3+1]
x[(T-1)*3+2]
shared [3] int x[(T*3)+3] where
T = THREADS
Example for array X as declared below:

## Slide 6: Fortran 2008 (CoArray or CAF)
Also compiler based one-sided program model
CoArray construct part of Fortran 2008 standard
Like SHMEM, currently supports only SPMD model
Address space model closer to SHMEM than UPC
But there is a significant complication with Fortran 2008 (and likely in future versions of UPC). Basically with Fortran 2008 not a clean separation between "shared" and "private" address spaces. See next slide.

## Slide 7: UPC/Fortran 2008(2)
.
#include <upc.h>
.
long *shared sh_ptr[THREADS];
long *my_mallocd_array = NULL;
long *thread_zeros_array = NULL;
if (MYTHREAD == 0) {
my_mallocd_array = (long *)malloc(1000 * sizeof(long));
sh_ptr[0] = my_mallocd_array;
}
upc_barrier(100);
if (MYTHREAD == 1) {
thread_zeros_array = sh_ptr[0];
for (int i=0;i<10;i++) thread_zeros_array[i] = 0xdeadbeef;
}
upc_barrier(101);
if (MYTHREAD == 0) {
for (int i=0;i<10;i++) assert(my_mallocd_array[i] == 0xdeadbeef);
}
Array of shared pointers to private long (likely preregistered with NIC)
This is not currently a legal UPC code example, but Fortran 2008 equivalent is. Just did not want to use Fortran for example.
private pointers to private long
Compiler translates this into an underlying RDMA get(load), including retrieval of mem reg info, etc.
Compiler translates into RDMA put

## Slide 8: Different Views of PGAS – implementing and using
Active Message Based Implementations
Pure (almost) one-sided implementations
Productivity more important than performance
Expect SHMEM, etc. to beat MPI on performance
implementer viewpoints
user viewpoints
Want to use SHMEM, etc. inside MPI app for performance reasons

## Slide 9: Some other animals in the one-sided program model zoo
Charm++ proxy
ARMCI proxy

## Slide 10: Community Feedback

## Slide 11: SHMEM/PGAS API Requirements – caveats and disclaimers
Assume significant degree of overlap with needs of MPI community, e.g.
  Similar needs with respect to supporting fork
  Similar needs concerning munmap if memory registration/deregistration needs to be managed explicitly by the SHMEM/PGAS runtime
What are covered here are API requirements more particular to SHMEM/PGAS and similar one-sided program models

## Slide 12: Memory Registration API Endpoint Considerations
Endpoint memory usage needs to be scalable
Low overhead mechanism for enumeration of endpoints, i.e. "ranks" rather than lids, etc.
It would be great to have connectionless (yet reliable)-style endpoints and interfaces, e.g. method in struct fi_ops_rma looks promising
If connected-style endpoints are the only choice, methods to do both on-demand and full-wire up efficiently would be great, e.g. both good performance of the struct fi_ops_av insert method as well as the struct fi_ops_cm connect/listen/accept methods.
API that supports "thread hot" thread safety model for endpoints.
int (*writemsg)(fid_t fid, const struct fi_msg_rma *msg, uint64_t flags);

## Slide 13: Memory Registration API Requirements (1)
Necessary evil?
  Some say yes if needed for good performance
Scalability of memory registration is a very important property
  API should be designed to allow for cases where only local memory registration info is required to access remote memory
  Does this lead to security issues? Have to have some protection mechanism.
An idea - let application supply “r_key” values to use - this idea is already in libfabric API - struct fi_ops_mr mr_reg method
On-demand paging option requirements
  Want flexibility to do on-demand paging when requested, but may also want “pinned” pages method, specified by application
  PGAS compiler has to have control of memory allocation to avoid needing this – but often compiler does have control of heap allocator, etc.
  Fortran 2008, possible future versions of UPC may still find this useful
  Maybe also be helpful for library based one-sided models, esp. if restrictions on what memory is remotely accessible become more relaxed

## Slide 14: Memory Registration API Requirements (2)
Fortran 2008 (CoArray) in particular could benefit from ability to register large amounts of virtual memory that may be only sparsely populated
Portals4 non-matching interface has an option which supports this if implementation supports PTL_TARGET_BIND_INACCESSIBLE
Compromise functionality where a large VM region can be “pre-registered” to prep I/O MMU and device driver, but does not pin pages. A second function would be called to pin/register segments of the region when remote memory access is needed.
Growable (both down and up) registrations would also be useful (mmap example)

## Slide 15: Small remote memory reference API requirements – perf and ops
PGAS compilers implemented directly on top of native RDMA functionality need an API that can deliver high performance for small non-blocking PUTs (stores) and GETs (loads). Typical remote memory accesses much smaller than for MPI programs and many more of them
Atomic memory ops are important (see later slide)
Put with various completion notification mechanisms:
  “signaling” put where a flag value is written by hw to a given location at target after all of the put data is visible in target memory
  atomic update option rather than simple flag write for remote notification
  Sender side notification for local completion (safe to reuse buffer) and global completion (data has at least reached global ordering point at target)
  Pointed out that global completion (not just global ordering point) can also be ascertained by initiator via any RDMA transaction that results in a non-posted request (RDMA get) at the target, at least for for PCI-e based hw.
Small partially blocking put requirement (till safe to reuse local buffer)
  Shmem on top of portals4/non-blocking puts semantics example – cost of implementing partially blocking on top of non-blocking?

## Slide 16: Small remote memory reference API requirements - ordering
PGAS compilers in particular have a special ordering requirement:
  Many PGAS compilers can benefit greatly from hardware which provides protection against WAW, WAR, and RAW hazards for remote memory references from a given initiator to a given target and address in the target’s address space.
.
#include <upc_relaxed.h>
.
void update_shared_array(shared long *g_array, long *local_data, int *g_idx, int nupdates)
{
int i;
for (i=0;i<nupdates;i++) {
g_array[g_idx[i]] += local_data[i];
}
upc_barrier(0);
if(MYTHREAD == 0) {
printf(“Done with work\n”);
}
}
app knows g_idx has no overlap between different threads, but possible repeat of indices for one thread, so no need for locks, etc. in update loop
Problem for compiler is here.
What if for some n,m it is the case that g_idx[n] == g_idx[m]. See notes.
Notes: The ordering issue here has to do with a compiler’s view of system memory. If a compiler is unable to assume if a store of a value X to address A in the system memory followed by load from the same address A does not return X, things get difficult. The same goes for the write after read and write after write cases.
This ordering guarantee can actually be difficult for PCI-e based network adaptors, even with a strictly in-order network to satisfy owing to PCI-e posted/non-posted request ordering rules.
As a workaround in such situations, things like hash tables and bloom filters can be used by the compiler to check for possible hazards of previously issued, but not completed remote memory transactions with ones about to be issued.
It would obviously be nice to have hardware solutions to this problem, and APIs that exposed the capabilities of such hardware.

## Slide 17: Small remote memory reference API requirements – Atomic memory ops
Rich set of AMOs also useful – need more than FADD and CSWAP.
Multi-element AMOs for active message support, etc.
Nice to have AMOs that can support MCS lock algorithm at scale – implies possibly needing 128 bit AMOs
At least two kinds of AMO performance characteristics:
  Low latency but reliable (either fail or succeed, result being reported back to initiator). This allows use of locks, queues, etc. without giving up on resilience to transient network errors.
  “At memory” computation, but only need a good enough answer. Throughput more important than reliability. Example is GUPS.
32/16 bit granularity ops would be useful in addition to 64 bit and possibly 128 bit.

## Slide 18: Small remote memory reference API requirements – AMO survey
Operation | IBM BG/Q | Cray XC | Quadrics SHMEM | IB
swap | x | x | x | -
comp & swap | x | x | x | x
masked swap | x | x (AFAX) | x | -
add | x | x | x | x
bitwise or | x | x | - | -
bitwise and | x | x | - | -
comp & or | x | - | - | -
comp & add | x | - | - | -
comp & or | x | - | - | -
comp & and | x | - | - | -
comp & xor | x | - | - | -
min | - | x | - | -
max | - | x | - | -

## Slide 19: Remote memory reference API requirements – completion notification
Lightweight completion notification is very desirable, especially for PUTs.
Ideally allow for batching of groups of PUT/GET requests with a single completion notification at the initiator.
Get completion information at target of the get operation:
  Data in the get buffer has been read and heading over the wire, i.e. target can reuse the buffer
  Data has arrived in initiator’s memory

## Slide 20: Large RDMA transfers
Not so different from MPI
Need RDMA read and write
Option for fences between transactions
Per transfer network ordering options would be great
Notification requirements similar to those for small remote memory references
For RDMA write - piggyback message data (more than 32 bits of imm data) coming along with bulk data – Gasnet request

## Slide 21: Collectives
Would be nice to not have to reinvent the wheel for multiple, often concurrently used program models, e.g. app using SHMEM and MPI
  A lower level common interface for frequently used collective operations – barrier, reductions, coalesce (allgather), alltoall
  Flat would be better, not have to do special on-node (within a cache coherent domain) operations within the SHMEM/PGAS implementation
//TODO: nothing defined in libfabric yet for collectives

## Slide 22: Active Message Support
Two general types of uses
  Lower performance need for RPC-like capabilities implied by some types of operations, e.g. upc_global_alloc
  Higher performance needed for PGAS languages implemented using an Active Message paradigm, as well as other active message based program models like Charm++
API should support sending of requests to pre-initialized queues, for which the target has registered callback functions to process the data sent from initiator. Payload can be restricted to small size ~256 bytes or less.
Initiator of message should get response back that message has arrived, optionally that message has been consumed by callback function
Implementation needs to be able to handle transient network errors, message is delivered once and only once to target
Some applications may require ordering of messages from a given initiator to given target, would be good to be able to specify this at queue initialization.
Flow control is important.
PAMI is a good example of an interface that meets many of these requirements

## Slide 23: References
http://openshmem.org/
BM Parallel Environment Runtime Edition Version 1 Release 2: PAMI Programming Guide (SA23-2273-03)
Using the GNI and DMAPP APIs
http://www.cs.sandia.gov/Portals/portals4-spec.html
http://www.openfabrics.org/downloads/OFWG/

## Slide 24: Thank You

## Slide 25: Backup Material

## Slide 26: UPC
Compiler based program model – ‘c’ with extensions
Each thread (PE in SHMEM model) has affinity to a certain chunk of shared memory
Objects declared as shared are allocated out of shared memory
Objects can be distributed across the chunks of shared memory in various ways – blocked, round robin, etc.
Collective operations, locks, etc.
Like MPI, evolving over time