## Slide 1: RSOCKETS
Sean Hefty
Intel Corporation

## Slide 2: Motivation (AKA the Problem)
VERBS

## Slide 3: More Specifically… Programming to Verbs
struct ibv_device **dev_list;
struct ibv_context *ib_ctx = NULL;
struct ibv_device_attr dev_attr;
struct ibv_port_attr port_attr;
int i, p, ret;
dev_list = ibv_get_device_list(NULL);
if (!dev_list)
error();
for (i = 0; dev_list[i]; i++) {
ib_ctx = ibv_open_device(dev_list[i]);
if (!ib_ctx)
error();
ret = ibv_query_device(ib_ctx, &dev_attr)
if (ret)
error();
Get a list of devices and their attributes

## Slide 4: More Specifically…
for (p = 1; p < dev_attr.phys_port_cnt; p++) {
ret = ibv_query_port(ib_ctx, i, &port_attr);
if (ret)
error();
if (port_attr.state == IBV_PORT_ACTIVE)
goto done;
}
ibv_close_device(dev_list[i]);
ib_ctx = NULL;
}
done:
ibv_free_device_list(dev_list);
if (!ib_ctx)
error();
Select a port and get its attributes

## Slide 5: More Specifically…
struct ibv_pd *pd;
struct ibv_comp_channel *comp_channel;
struct ibv_cq *cq;
pd = ibv_alloc_pd(ib_ctx);
if (!pd)
error();
comp_channel = ibv_create_comp_channel(ib_ctx);
if (!comp_channel)
error();
cq = ibv_create_cq(ib_ctx, min(min(MY_SQ_SiZE + MY_RQ_SIZE),
dev_attr.max_qp_wr), dev_attr.max_cqe),
NULL, comp_channel, 0);
if (!cq)
error();
We need : - protection domain - completion channel - completion queue

## Slide 6: More Specifically…
struct ibv_qp *qp;
struct ibv_qp_init_attr qp_init_attr;
qp_init_attr.send_cq = cq;
qp_init_attr.recv_cq = cq;
qp_init_attr.cap.max_send_wr = min(MY_SQ_SIZE, dev_attr.max_qp_wr / 2);
qp_init_attr.cap.max_recv_wr = min(MY_RC_SIZE, dev_attr.max_qp_wr / 2);
qp_init_attr.cap.max_send_sge = min(MY_SQ_SGE, dev_attr.max_sge);
qp_init_attr.cap.max_recv_sge = min(MY_RQ_SGE, dev_attr.max_sge);
qp_init_attr.sq_sig_all = 1;
qp_init_attr.qp_context = NULL;
qp_init_attr.qp_type = IBV_QPT_RC;
qp = ibv_create_qp(pd, &qp_init_attr);
if (!qp)
error();
- and a queue pair

## Slide 7: More Specifically…
void *msgs;
struct ibv_mr *mr;
msgs = calloc(qp_init_attr.cap.max_recv_wr, MY_MSG_SIZE);
if (!msgs)
error();
mr = ibv_reg_mr(pd, msgs, qp_init_attr.cap.max_recv_wr * MY_MSG_SIZE,
IBV_ACCESS_LOCAL_WRITE);
if (!mr)
error();
Allocate some messages to receive data…
and register them with the device

## Slide 8: More Specifically…
struct ibv_recv_wr recv_wr, *bad_wr;
struct ibv_sge sge;
recv_wr.next = NULL;
recv_wr.sg_list = &sge;
recv_wr.num_sge = 1;
recv_wr.wr_id = 0;
sge.length = MY_MSG_SIZE;
sge.lkey = mr->lkey;
sge.addr = msgs;
for (i = 0; i < qp_init_attr.cap.max_recv_wr; i++) {
ret = ibv_post_recv(qp, &recv_wr, &bad_wr);
if (ret)
error();
sge.addr += MY_MSG_SIZE;
}
Post the messages on the queue pair *before* we connect

## Slide 9: More Specifically…
I only have 30 minutes
and want to transfer data
assume we connect

## Slide 10: More Specifically…
void *msg;
struct ibv_mr *mr;
msg = calloc(1, MY_MSG_SIZE);
if (!msg)
error();
mr = ibv_reg_mr(pd, msg, MY_MSG_SIZE,
IBV_ACCESS_LOCAL_WRITE);
if (!mr)
error();
Allocate a send buffer…
and register it with the device

## Slide 11: More Specifically…
struct ibv_send_wr send_wr, *bad_wr;
struct ibv_sge sge;
send_wr.next = NULL;
send_wr.sg_list = &sge;
send_wr.num_sge = 1;
send_wr.wr_id = 0;
sge.length = MY_MSG_SIZE;
sge.lkey = mr->lkey;
sge.addr = msgs;
<format_msg(msgs, 0);>
ret = ibv_post_send(qp, &send_wr, &bad_wr);
if (ret)
error();
All this just to send?

## Slide 12: More Specifically…
struct ibv_wc wc;
struct ibv_cq *cq;
void *context;
int ret;
do {
ret = ibv_poll_cq(cq, 1, &wc);
if (ret)
break;
ret = ibv_req_notify_cq(cq, 0);
if (ret)
error();
ret = ibv_poll_cq(cq, 1, &wc);
if (ret)
break;
Wait for the send to complete or we receive a response
Remember to poll the completion queue after requesting notification

## Slide 13: More Specifically…
ret = ibv_get_cq_event(comp_channel, &cq, &context);
if (ret)
error();
ibv_ack_cq_events(cq, 1);
} while (1);
if (ret < 0)
error();
Wait for an event and check the completion queue again
And it’s just that easy to send data!

## Slide 14: Motivation continued
And it’s just as bad on the receive side
Now, anyone want to DO an actual RDMA operation?

## Slide 15: Motivation continued
Actually, I just wanted to echo typing between two systems connected by IB that did not have ipoib (or sdp) but this wouldn’t make as good an intro

## Slide 16: Big Intro…
RDMA sockets API
  Another API - ~joy~
Calls that look and behave like sockets
Connects like sockets
Byte streaming transfers like sockets
  I.e. SOCK_STREAM
Support for nonblocking operation like sockets
Ta-da!
Like sockets … except that it’s not
RSOCKETS!

## Slide 17: Goals
Socket programming concepts with minimal to no need to learn anything about RDMA
  Let’s face it, no matter how many APIs we create developers will still learn sockets
  Sockets will continue as the common fallback API
Support existing socket applications under ideal conditions
SDP license free!
Support well-known network programming concepts

## Slide 18: Goals
Outperform ipoib (and sdp)
  Or it’s pointless, except for limited environments
Perform favorably compared to native RDMA implementation
  Or there’s not a strong enough reason NOT to learn RDMA programming
  Narrow the cost-benefit gap of maintaining verbs support in an application long term
High performance

## Slide 19: RSOCKETS Overview
Proprietary protocol / algorithm
  I made it up
  Will be open sourced
Entirely user-space implementation
  Well, if we ignore the existing RDMA support
  No need to merge anything upstream!
RSOCKETS
Verbs
RDMA CM
RDMA Device
Kernel bypass

## Slide 20: R + SOCKET Interface
Connections
rsocket, rbind, rlisten, raccept, rconnect
rshutdown, rclose
Data transfers
rrecv, rrecvfrom, rrecvmsg, rread, rreadv
rsend, rsendto, rsendmsg, rwrite, rwritev
Asynchronous support
rpoll, rselect
Socket options
rsetsockopt, rgetsockopt, rfcntl
Other useful calls
rgetpeername, rgetsockname

## Slide 21: Supported Features
Functions take same parameters as sockets
PF_INET, PF_INET6, SOCK_STREAM, IPPROTO_TCP
MSG_DONTWAIT, MSG_PEEK
SO_REUSEADDR, TCP_NODELAY, SO_ERROR
O_NONBLOCK
SO_SNDBUF, SO_RCVBUF
Implementation based on needs of OSU and Intel MPI

## Slide 22: Now a word from our sponsor…
INFORMATION IN THIS DOCUMENT IS PROVIDED “AS IS”. NO LICENSE, EXPRESS OR IMPLIED, BY ESTOPPEL OR OTHERWISE, TO ANY INTELLECTUAL PROPERTY RIGHTS IS GRANTED BY THIS DOCUMENT. INTEL ASSUMES NO LIABILITY WHATSOEVER AND INTEL DISCLAIMS ANY EXPRESS OR IMPLIED WARRANTY, RELATING TO THIS INFORMATION INCLUDING LIABILITY OR WARRANTIES RELATING TO FITNESS FOR A PARTICULAR PURPOSE, MERCHANTABILITY, OR INFRINGEMENT OF ANY PATENT, COPYRIGHT OR OTHER INTELLECTUAL PROPERTY RIGHT.
Performance tests and ratings are measured using specific computer systems and/or components and reflect the approximate performance of Intel products as measured by those tests. Any difference in system hardware or software design or configuration may affect actual performance. Buyers should consult other sources of information to evaluate the performance of systems or components they are considering purchasing. For more information on performance tests and on the performance of Intel products, reference www.intel.com/software/products.
Intel and the Intel logo are trademarks of Intel Corporation in the U.S. and other countries.
*Other names and brands may be claimed as the property of others.
Copyright © 2012. Intel Corporation.

## Slide 23: More words from our sponsor…
Optimization Notice
Intel’s compilers may or may not optimize to the same degree for non-Intel microprocessors for optimizations that are not unique to Intel microprocessors. These optimizations include SSE2, SSE3, and SSSE3 instruction sets and other optimizations. Intel does not guarantee the availability, functionality, or effectiveness of any optimization on microprocessors not manufactured by Intel. Microprocessor-dependent optimizations in this product are intended for use with Intel microprocessors. Certain optimizations not specific to Intel microarchitecture are reserved for Intel microprocessors. Please refer to the applicable product User and Reference Guides for more information regarding the specific instruction sets covered by this notice. Notice revision #20110804
8-node Xeon X5570 @ 2.93 Ghz (Nehalem) cluster
8 cores / node
40 Gbps Infiniband
2 node latency and BW tests rstream / perftest
64 process MPI runs

## Slide 24: What’s the Performance?
Promising latency and bandwidth
Can it work with existing apps? At all? Well?
Chart: 64-Byte Ping-Pong Latency (us)
| IPoIB | SDP | RSOCKET | IB
 | 19.57 | 4.21 | 1.71 | 1.33
Chart: Bandwidth (Gbps)
| 64 | 128 | 256 | 512 | 1k | 2k | 4k | 8k | 16k | 32k | 64k | 128k | 256k | 512k | 1m
IPoIB | 0.47 | 0.93 | 1.68 | 3.27 | 4.59 | 5.98 | 6.94 | 7.84 | 8.15 | 8.41 | 8.52 | 8.64 | 8.84 | 9.02 | 9.02
SDP | 0.09 | 0.18 | 0.37 | 0.72 | 1.42 | 2.75 | 5.23 | 9.41 | 15.43 | 18.49 | 22.39 | 7.15 | 9.56 | 12.04 | 12.2
RSOCKET | 1.19 | 2.56 | 4.8 | 8.84 | 14.26 | 21.98 | 22.53 | 23.36 | 24.08 | 24.46 | 24.72 | 24.72 | 24.72 | 24.72 | 24.72
IB | 1.9 | 3.808 | 7.816 | 16.176 | 23.416 | 24.696 | 25.264 | 25.488 | 25.696 | 25.776 | 25.824 | 25.824 | 25.824 | 25.824 | 25.824
N/2: 500 vs 650 B
Note: implementation has minimal optimizations

## Slide 25: Supporting Existing Apps
MPI or socket application
LD_PRELOAD RSOCKET conversion library
RSOCKET
RDMA Verbs
RDMA CM
Socket API
Real Socket API
Limited fallback support
Export socket calls and map them to rsockets

## Slide 26: IMB - Intel MPI Benchmarks
Measure important MPI functionality
Results for arbitrarily selected sizes
IPoIB performance was much worse
  Omitted for space
SDP tests failed for 64 ranks
  Had lower performance for fewer ranks
Results in microseconds - lower is better

## Slide 27: IMB Results
Chart: IMB 64 B (us)
| Allgather | Allgatherv | Alltoall | Alltoallv
RSOCKETS | 47.44 | 45.91 | 120.06 | 171.66
OFA | 57.07 | 48.9 | 97.02 | 113.07
Chart: IMB 64 B (us)
| PingPong | PingPing | Sendrecv | Exchange | Allreduce | Reduce | Reduce_scatter | Gather | Gatherv | Scatter | Scatterv | Bcast | Barrier
RSOCKETS | 8.22 | 16.68 | 4.71 | 7.04 | 28.82 | 26.69 | 16.39 | 25.85 | 214.13 | 10.38 | 43.94 | 7.58 | 19.01
OFA | 1.91 | 6.4 | 3.1 | 3.54 | 26.19 | 13.56 | 17.94 | 29.53 | 18.97 | 7.12 | 31.61 | 5.34 | 18.41
Chart: IMB 4 KB (us)
| Allgather | Allgatherv | Alltoall | Alltoallv
RSOCKETS | 1088.46 | 865.43 | 2097.03 | 2111.19
OFA | 835.61 | 1417.88 | 2104.99 | 2120.17
Chart: IMB 4 KB (us)
| PingPong | PingPing | Sendrecv | Exchange | Allreduce | Reduce | Reduce_scatter | Gather | Gatherv | Scatter | Scatterv | Bcast
RSOCKETS | 37.25 | 407.44 | 17.31 | 33.12 | 86.21 | 103.9 | 46.04 | 29.6 | 169.66 | 29.34 | 106.42 | 21.64
OFA | 28.36 | 354.59 | 14.78 | 30.51 | 94.07 | 57.09 | 50.57 | 655.89 | 47.65 | 546.84 | 111.69 | 24.38

## Slide 28: IMB Results
Chart: IMB 64 KB (us)
| PingPong | PingPing | Sendrecv | Exchange | Allreduce | Reduce | Reduce_scatter | Gather | Gatherv | Scatter | Scatterv | Bcast
RSOCKETS | 9.23 | 18.86 | 197.96 | 454.33 | 488.89 | 624.13 | 264.66 | 392.35 | 697.26 | 317.31 | 1153.75 | 218.51
OFA | 1.98 | 6.6 | 246.08 | 498.81 | 746.55 | 1121.32 | 716.4 | 1120.28 | 1803.38 | 769.61 | 1020.05 | 313.61
Chart: IMB 64 KB (us)
| Allgather | Allgatherv | Alltoall | Alltoallv
RSOCKETS | 13199.59 | 12972.5 | 17105.84 | 17083.8
OFA | 15900.48 | 15802.21 | 14538.42 | 14527.77
Chart: IMB 1 MB (us)
| PingPong | PingPing | Sendrecv | Exchange | Allreduce | Reduce | Reduce_scatter | Gather | Gatherv | Scatter | Scatterv | Bcast
RSOCKETS | 51.07 | 709.63 | 3195.36 | 6834.17 | 7668.15 | 4702.48 | 4087.1 | 14658.56 | 17157.25 | 5985.45 | 6197.03 | 3449.74
OFA | 31.06 | 364.88 | 3208.43 | 6813.72 | 7007.21 | 4446.57 | 4661.89 | 18653.18 | 20202.6 | 20795.82 | 22597.75 | 3075.17
Chart: IBM 1 MB (us)
| Allgather | Allgatherv | Alltoall | Alltoallv
RSOCKETS | 209177.06 | 208600.6 | 257261.97 | 276003.36
OFA | 203313.9 | 202948.73 | 214664.28 | 242797.9

## Slide 29: What About a “Real” App?
HPC Challenge benchmarks
  Set of higher-level benchmarks
As close to a “real” app that I could easily run
Selected results reported
  SDP failed to run
  IPoIB results included

## Slide 30: HPC Challenge
Chart: HPCC Latency (us)
| MaxPingPong | RandomRing | MinPingPong | AvgPingPong | NaturalRing
TCP | 21.3832 | 40.1171 | 2.9355 | 17.4155 | 38.0993
RSOCKETS | 6.0052 | 6.3082 | 2.2501 | 4.1072 | 4.7922
OFA | 2.1756 | 4.3945 | 1.5646 | 1.8659 | 4.1008
Chart: HPCC Bandwidth (GB/s)
| MinPingPong | NaturalRing | RandomRing | MaxPingPong | AvgPingPong
TCP | 0.70874 | 0.012793 | 0.012972 | 4.6838 | 1.281
RSOCKETS | 2.4245 | 0.32069 | 0.28309 | 3.115 | 2.7973
OFA | 2.5756 | 0.32792 | 0.29467 | 3.3334 | 3.0837
Higher is better
Lower is better

## Slide 31: HPC Challenge
Chart: HPL (Tflops)
| TCP | RSOCKETS | OFA
 | 0.48075 | 0.61845 | 0.61777
Chart: PTRANS (GB/s)
| TCP | RSOCKETS | OFA
 | 1.3564 | 10.2858 | 9.8419
Chart: MPI Random Access LCG (GUPs)
| TCP | RSOCKETS | OFA
 | 0.012554 | 0.0062638 | 0.050413
Chart: MPI FFT (Gflops)
| TCP | RSOCKETS | OFA
 | 3.4065 | 26.6067 | 28.5322
Look over there
Higher is better

## Slide 32: Closing the Performance Gap
Notable area for improvement:
  Direct data placement (reduce memory copies)
Possible, but…
Most target applications use nonblocking sockets
  Restricts use with recv()
  Which reduces usefulness with send()
Alternatives?

## Slide 33: Closing the Performance Gap
Is there any way to add direct access to RDMA operations through sockets?
  Get that last bit of performance
While keeping it simple?
And.. without actually needing to know anything about RDMA?
  Or these acronyms: PD, CQ, HCA, MR, QP, LID, GID, …
And make it generic, so that other technologies may be able to use it
  Tag matching, file I/O, SSDs
And continue to support the socket programming model!

## Slide 34: Direct Data Placement Extensions
Can we find calls that blend in with existing calls?
Now we may be talking about new programming concepts
Are there any existing calls that are usable?
  send, sendto, sendmsg, write, writev, pwrite …
  recv, recvfrom, recvmsg, read, readv, pread …
  mmap, lseek, fseek, fgetpos, fsetpos, fsync …
This is a discussion point only
Although not used with sockets, these calls may be used as guides

## Slide 35: Direct Data Placement APIs
rmmap
Specify access restrictions
rget
Read from an offset into a local buffer
rput
Write from a local buffer to the given offset
Maps to RDMA read operation
Maps to RDMA write operation
Map memory to a specified offset
Maps to memory registration

## Slide 36: Direct Data Placement
Extends current usage model
  No change to connecting or send/recv calls
  Memory region data exchanged underneath
Appears usable for multiple technologies
Seems easy to learn and use
Sounds great, you should get to work on this right away!

## Slide 37: The Real Problem
Target applications use nonblocking sockets
Direct data placement calls may not block
Notification of completion should come from select() and poll() calls
Would need to determine how to handle nonblocking calls without an indecent exposure to RDMA

## Slide 38: Requests to Verbs
Asynchronous memory registration
  Assist with direct data placement
A single file descriptor for all RDMA resources
  Event queue, completion queue, connections
  Simplifies implementation
Way to transfer control of a set of RDMA resources to another process
  Help support apps that fork

## Slide 39: What’s Your Opinion?
Does rsockets have a place going forward?
It’s really 5 years too late
In limited environments
Absolutely
What’s the best way to add direct data placement?
Not at all
Best solution using existing socket calls
Extensions
What other features are worth implementing?
Datagram support?
Out of band data?
Fork?

## Slide 40: thank_you; exit(0);