## Slide 1: Discussing an I/O Framework
SC13 - Denver

## Slide 2
The OpenFabrics Alliance has recently undertaken an effort to review the dominant paradigm for high performance I/O, beginning with the application interface.
The existing paradigm is the Verbs API running over an RDMA network.
The OFA chartered a new working group, the OpenFramework Working Group (OFWG) to:
  Develop, test, and distribute:
    Extensible, open source interfaces aligned with application demands for high-performance fabric services.
    An extensible, open source framework that provides access to high-performance fabric interfaces and services.

## Slide 3: (potential) objectives for the BoF
This is a pretty new effort, so we’re not sure what color feathers the birds will be wearing.
We want to keep this BoF very interactive, but also responsive to attendees needs.
Couple of directions we could take today
Introduce the basic concepts and familiarize us all with the background behind this new effort, or
Dive into details by picking up the discussion where we left off at our last meeting

## Slide 4: BoF Topics – pick one
What is the OFWG
Motivations for creating the OFWG
Why a new framework?
Fabric Interfaces
I/O Services
Application-centric I/O - a user-driven process
What is meant by an I/O service
What happens to the familiar Verbs API

## Slide 5: What is the OFWG?

## Slide 6: OpenFramework Working Group
Created by the OpenFabrics Alliance on August 16, 2013
Charter
Develop, test, and distribute
    An extensible, open source framework that provides access to high-performance fabric interfaces and services.
    Extensible, open source interfaces aligned with ULP and application needs for high-performance fabric services
Work with standards bodies as needed to create interoperability; the OFA will not itself create industry standards
Working methods
  Facilitated by the open source community,
  But driven by application requirements

## Slide 7: OFWG direction
Evolve the verbs framework into a more generic open fabrics framework
  Fold in RDMA CM interfaces
  Merge kernel interfaces under one umbrella
Give users a fully stand-alone library
  Design to be redistributable
Design in extensibility
  Based on verbs extension work
  Allow for vendor-specific extensions
Export low-level fabric services
  Focus on abstracted hardware functionality

## Slide 8: Why was the OFWG created?

## Slide 9: High level
There are three reasons for doing so:
Increasing scale of HPC systems  mathematical modeling
Emerging uses of computation that did not exist 10 years ago  data modeling
Demand for collaboration  evolving data access and storage requirements
Improve the “fit” of high performance networks to modern applications

## Slide 10: Evolving uses (short list)
Compute: Larger, more complex problems in mathematical modeling
Analyze: Ingest, sort and process avalanches of unstructured data – data modeling
Store: Access and store data in new ways
In short, “application requirements” continue to shift over time
Notes: Problem Space – New usages driving new application requirements. And we want to broaden the OFA’s appeal.
There are significant changes in the way computer systems are used. This may change the way applications access and use I/O services, leading to further splintering of the clean verbs interface. For example, Big Data usages require access to unstructured data. Or Cloud Computing requires a pool of storage accessible over the web. Or scientists collaborating over extremely large data sets require methods to share access to a single storage repository. E.g. Sq Km Array

## Slide 11: RDMA today
Hardware Layer
Application layer
Upper layer protocols
RDMA Provider Layer
Verbs API
There is some splintering today around the way that applications access available RDMA I/O services.
Some applications
are coded to the Verbs API,
Some are coded directly to the low level hardware,
Some use an ‘adaptation layer’ to hide the network
Notes: Problem space: A splintering of the I/O interface?
OFA began by implementing a single, clean interface: the Verbs API based on the Verbs specification. Over time, a series of ULPs have been added to smooth and accelerate the adoption of RDMA. Thus, today we have several ‘interfaces’ to the RDMA service to meet different needs. For lowest latency, code to the verbs. For block storage access, use the SRP or iSER ULPs. Eventually PSM emerged as a higher performance interface mainly for MPI applications. We are seeing a slight splintering of the interface layer.

## Slide 12: Neo-classical data transformation
Data
Information
Intelligence
(delay)
(delay)
(delay)
Unstructured data
analyze
decision
Ingest and reduce
sophisticated analytics
rapid, complex decision-making
Data Modeling (“Big Data”) is emerging. Do data modeling applications (e.g. reduction operations, analytics, etc) have unique I/O requirements? Are they well served by the current verbs interface?
Action
Notes: The point is simple – computing as we know it has evolved dramatically.
Big data techniques in ingesting and reducing large amounts of unstructured data
Analytics techniques in addition to classical clusters or mainframes for data analysis
Much faster decision making systems

## Slide 13: Detailed claims
Verbs is an imperfect semantic match for industry standard APIs (MPI, PGAS, ...)
ULPs continue to desire additional functionality
  Difficult to integrate into existing infrastructure
OFA is seeing fragmentation
  Existing interfaces are constraining features
  Vendor specific interfaces

## Slide 14: Why a new framework

## Slide 15: Current verbs-based framework
Device(s)
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocols
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
60 function calls in libibverbs
a series of kernel services
Support for multiple vendors,
Support for multiple fabrics
Applicaton adaptation layer

## Slide 16: Current verbs-based framework
Oriented around the Verbs semantics defined in the IB Architecture specs
Verbs defines a very specific set of I/O services.
Basic abstraction exported to an application is a queue pair
A queue pair is configured to provide an operation (send/receive, write/read, atomics…) over one of a set of services (reliable, unreliable…)
Low level fabric details (e.g. connection management) are exposed to the application layer

## Slide 17: New framework
Provide a richer set of services, better tuned to application requirements
Increase the number of APIs, but simplify each API by reducing the functions associated with it – every conceivable function is not necessarily available to each API
APIs are composable, and can be combined
Abstract the low level fabric details visible to the application

## Slide 18: A framework
Fabric Interfaces
I/F
I/F
I/F
I/F
Fabric Provider Implementation
I/O service
I/O service
I/O service
Framework defines multiple interfaces
Vendors provide optimized implementations
The framework exports a number of I/O services (e.g. message passing service, large block transfer service, collectives offload service, atomics service…) via a series of defined interfaces.
* Important point! The framework does not define the fabric.
…
Notes: Solution Space – provide a framework allowing applications to select the appropriate I/O service(s), and allowing vendors to select which I/O services to implement.

## Slide 19: A framework
Fabric Interfaces
I/F
I/F
I/F
I/F
Fabric Provider Implementation
I/O service
I/O service
I/O service
Framework defines multiple interfaces
Vendors provide optimized implementations
* Important point! The framework does not define the fabric.
…
Each interface exports one or more I/O services
An I/O vendor chooses how to optimally implement the services he chooses to provide
Notes: Solution Space – provide a framework allowing applications to select the appropriate I/O service(s), and allowing vendors to select which I/O services to implement.

## Slide 20: Fabric Interfaces

## Slide 21: (Scalable) Fabric Interfaces
Q: What is implied by incorporating interface sets under a single framework?
  Objects exist that are usable between the interfaces
    Isolated interfaces turn the framework into a complex dlopen
  Interfaces are composable
    May be used together
Fabric Interfaces
Message Queue
Control
Interface
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services

## Slide 22: I/O service

## Slide 23: User mode RDMA services
Verbs function calls
RDMA service provider
IB
Enet
IP/Enet
Reliable service
Unreliable service
remote memory access service
unicast msg service
(send/rcv)
multicast msg service
atomic operation service
QP
one API (verbs)
Multiple services provided by each provider.
three wire protocols
QP is a h/w construct effectively representing one HCA (or NIC or RNIC) port
app
I/F
Characteristics of the QP ‘bleed through’ the i/f to the app
QP abstracts the entire set of services, whether they are needed or not

## Slide 24: I/O services
Fabric interface
i/f
Fabric service
Reliable service
IB
Enet
IP/Enet
Unreliable service
remote memory access service
unicast msg service
multicast msg service
atomic operation service
APIs expose the semantics of the underlying fabric service(s) directly
Multiple service providers.
Vendors innovate in implementing and optimizing services
wire protocols
i/f
i/f
i/f
…

## Slide 25: Control Interface
fi_getinfo
Discover fabric providers and services
Identify resources and addressing
fi_socket
Allocate fabric communication portal
fi_open
Open resource domain and interfaces
fi_register
Dynamic providers publish control interfaces
FI Framework
fi_getinfo fi_freeinfo
fi_socket fi_open
fi_register

## Slide 26: Verbs compatibility

## Slide 27: What is compatibility?
Assertion - the libibverbs library continues to exist
How important is it to retain compatibility with verbs?
If it is, what does compatibility mean?
- Binary compatibility – applications continue to run exactly as today
(too limiting?)
- Recompile the application targeting a new library
- Retain existing services, but not the same function calls
- Provide migration paths for both applications and providers

## Slide 28: Proposal (for discussion)
Device(s)
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocols
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
The verbs framework goes away,
But verbs functionality remains
Reliable service
Unreliable service
remote memory access service
unicast msg service
multicast msg service
atomic operation service

## Slide 29: Application-centric I/O

## Slide 30: Application-centric I/O
app
app
i/f
Fabric provider
i/f
Fabric provider
“Application-centric I/O” is the art and science of defining an I/O system that maximizes application effectiveness.”

## Slide 31: Historical RDMA design flow
App reqmts (e.g. low latency) drove fabric characteristics
IBTA specified an RDMA service:
  send/receive,
  RDMA RD. RDMA WRT…
OFA implemented the API
app
RDMA
Service
Verbs API
1
2
3
In the case of OFA, the RDMA Service was designed first (including the Verbs specification), followed by the Verbs API. This is still an application-centric approach to I/O.
other
services
technology specific fabric*
Notes: Designing an Application-centric I/O service.
Even though the RDMA service was defined first, this is STILL an application-centric I/O, it just happens that the interface (the verbs API) was defined *after* the fabric had been specified. So yes, it is a “bottoms up approach” to designing an application-centric I/O architecture.

## Slide 32: Application interfaces
Hardware Layer
Application Interface
Application layer
Provider Layer
Understand I/O characteristics of the applications of interest
Let those characteristics drive the interface definition(s)
Which ultimately drives the fabric feature set(s)
“Application-centric I/O” means that application reqmts drive the I/O system design
Notes: Solution Space – apply the principles of Application-centric I/O rigorously.
An Example: an MPI application may require the provider layer to provide a collectives service.

## Slide 33: Classic OFS Architecture (simplified)
Device
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocol
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access

## Slide 34: Classic OFS Architecture (simplified)
Device
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocol
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Legacy apps (skts, IP)
Data Analysis
Data Storage, Data Access
Distributed Computing
Filesystems
Object storage
Block storage
Distributed storage
Storage at a distance
Via msg passing
MPI applications
Structured data
Unstructured data
Skts apps
IP apps
Via shared memory
- PGAS languages

## Slide 35: Useful contacts
OpenFabrics Alliance – www.openfabrics.org
OpenFramework Working Group - http://lists.openfabrics.org/cgi-bin/mailman/listinfo
OpenFramework Working Group co-chairs –
Paul Grun (Cray, Inc.) grun@cray.com
Sean Hefty (Intel) sean.hefty@intel.com

## Slide 36: Thank You