## Slide 1: Fabtests – test framework ideas/suggestions
Howard Pritchard – LANL LA-UR-1426578

## Slide 2: Topics
Current state of fabtests
Test suites for similar RDMA network protocols
  OFED tarball
  PAMI
  Portals4
  uGNI
HPC-style job launcher options
Content ideas for fabtests

## Slide 3: Fabtests – current state
Only two tests currently
  unit/provinfo.c – tests fi_getinfo
  simple/pingpong.c – tests FI_MSG based ping/pong using client/server model
Need a lot more – we all know this

## Slide 4: OFED 3.1.2 tarball
perftest-2.2-0.17
  Set of client/server based tests of send/recv, rdma performance, etc.
  Simple job launch script for client side
qperf-0.4.9
  Client/server style tests for UC,UD,RC send/recv, rdma (amos) performance
Doesn’t appear to be any src rpm containing a set of unit tests for ibverbs or psm in the OFED 3.1.2 tarball

## Slide 5: PAMI – finding it
Little tricky to find, but available at https://repo.anl-external.org/repos/bgq-driver/V1R2M2/
Get the brq-V1R2M2.tar.gz tarball

## Slide 6: PAMI testsuite
The PAMI tests will untar into comm/sys/pami/tests
Lots of them, for collectives, p2p, PAMI internal funcs, etc. Perf tests and unit tests appear to be intermingled.
Appears all tests are launched on BG using poe

## Slide 7: Portals4
At code.google.com/p/portals4
About 30 basic tests, can be used either for matching or non-matching portals NIC handle
Also have several performance tests (e.g. NetPIPE, portals versions of Sandia MPI Benchmarks - SMB, …)
Leverages Argonne Hydra/simple PMI job launcher for basic runtime support, included in the Portals tarball

## Slide 8: GNI (Cray)
Lots of unit tests for in the unit tests rpm (generally not available to customers), generally written by developers of particular GNI features
Also have an examples rpm intended for customers to provide guidance on using GNI – not written by the developers
With a few exceptions, all of the tests and examples use Hydra-lite(or Cray aprun)/PMI for a runtime system

## Slide 9: HPC-style runtime/job launcher and fabtests
The libfabric API does not require a HPC-style runtime/job launch – this is a good thing
However, for most HPC use cases, some kind of runtime/job launch system will be used
Having such a runtime system makes writing unit/example tests reflecting HPC use cases much easier
  Can run tests on production systems without interfering with other users
  Provides ways for exchanging info in an OOB way between processes running a test

## Slide 10: Job launcher options for fabtests
Roll our own using pdsh, etc.
  May be more familiar to non-HPC users
  To HPC users, may seem like wheel reinventing
HPC job launch options
  Resource manager specific job launchers
    SLURM, LFS, etc.
    Vendor specific (Cray aprun, IBM poe, etc.)
  Open source options
    Hydra (Argonne’s MPICH job launcher)
    ORTE (OpenMPI’s job launcher)
    YARN - Hadoop (this is kind of a joke)

## Slide 11: Hydra and ORTE Compared
 | Hydra/Simple PMI | ORTE
License | BSD style | BSD style
Packaging | Job launcher for MPICH. Available as a separate package. Simple PMI included in MPICH | Comes as part of OpenMPI package.
Batch system/launcher aware | yes | yes
Ease of use within fabtests | Simple, high level PMI interface | More complex, lower level interface, likely would require a glue layer of some sort to avoid libfabric developers/testers having to learn ORTE/OPAL

## Slide 12: Hydra & PMI
Job launch
  mpiexec –n 2 –hosts node1,node2 ./a.out
Basic job setup and parameters
  PMI_Init/PMI_Finalize
  PMI_Rank
  PMI_Size
Barrier function (PMI_Barrier)
Key-value store
  PMI_KVS_put/PMI_KVS_get
  PMI_KVS_commit

## Slide 13: Content Ideas for fabtests

## Slide 14: Job launcher related tests
Add Hydra/simple PMI to fabtests, much like is provided with Portals4
Include some simple smoke tests which only exercise the PMI functionality. If these don’t work, no sense running fabtests which rely on Hydra/PMI.

## Slide 15: Provider checklist tests

## Slide 16: Endpoint types
According to fabric.7 man page, a provider must support at least one of the following endpoint types for libfabric version 1
FID_MSG | connected/reliable
FID_RDM | unconnected/reliable
FID_DGRAM | unconnected/unreliable

## Slide 17: Endpoint data transfer/CM functionality
Provider must implement at a minimum the FI_MSG data transfer interface
Connection management functions for FID_RDM/FID_DGRAM: getname, getpeer, connect, multicast join/leave
Connection management functions for FID_MSG: getname, getpeer, connect, accept, listen, reject, shutdown

## Slide 18: Access Domain Functionality
Must support opening address vector maps and tables
Address vectors (AVs) have to support at least FI_ADDER_PROTO input format, FI_SOCKADDR_IN(6) if endpoints can be identified by IP addr
AVs must support must support following output formats: FI_ADDR, FI_ADDR_INDEX, FI_AV
Must support opening EQs and counters

## Slide 19: Event Queue Functionality
Must support at least FI_EQ_FORMAT_CONTEXT
Data transfer completion EQs must support the FI_EQ_FORMAT_DATA format

## Slide 20: Forward compatibility
Provider expected to be forward compatible
Able to handle being compiled against expanded fi_xxx_ops….

## Slide 21: Other ideas
Example tests illustrating non-trivial usage of various endpoint types
Error handling – simulating error events being delivered to a COMP EQ, etc.
Out of order deliver simulation
Move fabtests project to github or other location more suitable for open source development

## Slide 22
BACKUP MATERIAL

## Slide 23: Hydra / ORTE Compared
Hydra
  BSD style license
  Separate package from MPICH
  Works with simple PMI client (the app)
  “template” already with Portals4 package
  Simple to use PMI interface
  Batch system aware
ORTE
  BSD style license
  Part of OMPI package/uses OPAL
  More complex to use than Hydra/PMI – at least looking at ORTE tests
  Batch system aware