## Slide 1: Persistent Memory over Fabric (PMoF) Architecture Overview NVML Implementation & Use Cases 08/08/17
Chet Douglas – DCG NVMS SW Architecture

## Slide 2: RDMA with byte-addressable PM – Problem Statement
HA and HPC Use Cases require writes to remote memory between compute nodes utilizing RDMA to support remote data base log updates, remote data replication, etc
Customers are requesting mechanisms to utilize RDMA with persistent memory NVDIMMs
Current RDMA HW and SW solutions do not take persistent memory in to account and do not have an explicit mechanism for forcing RDMA Writes to remote pmem to be persistent before the write’s completion
In the short term, SW only modifications are possible to make RDMA SW Applications persistent memory aware and to force written data to be persistent (PMoF 1.0 for current platforms)
In the longer term, industry wide enabling through standards organizations is required to have specific vendor agnostic mechanisms for utilizing persistent memory with RDMA, requiring HW and SW changes (future PMoF HW/FW/SW additions for future HW platforms)

## Slide 3: RDMA with byte-addressable PM – Problem Statement
RDMA with PMEM adds additional complexity:
  In order to guarantee written data is durable on the target node, CPU caches need to be bypassed or flushed to get data in to the ADR power fail safe domain
  When writing to PMEM, need a synchronous acknowledgement when writes have made it to the durability domain but the current RDMA Write semantics do not provide such write acknowledgement

## Slide 4: PMoF Overview –Overview of DAX Programming Model
AEP NVDIMM
Persistent Region – App Direct Mode
User
Space
Kernel
Space
DAX
Application
load store movnt
clflushopt clwb
Standard
File API
Persistent Memory Aware File System
MMU
Mappings
Cache Line I/O
Apache Pass
PMEM Programming Model
open close mmap msync
DAX
Removes paging IO subsystem & provides direct access to PMEM
SNIA NVM Programming Model
Byte Addressable PMEM Regions surfaced directly to an application through standard Memory Mapped Files
Standard File API utilized to create, open, close, memory map, and synchronize a file
Applications have direct control over load and store from/to the memory mapped file
Applications are responsible for flushing write data in CPU caches in to the persistent memory domain
  clflushopt – cache line flush and invalidate – non temporal, flushes can occur in parallel and require SFENCE after all flushed
  clwb – cache line write back

## Slide 5: PMoF Overview –Overview of Durability Domain

## Slide 6: PMoF Overview – NVML Overview
Ring-3 application programming library
Simplifies NVM programming
Provides persistent memory allocation, de-allocation
Persistent power fail safe transactions and ability to undo transactions that fail
Currently available on 64bit Linux via GitHub. See http://pmem.io
NVML is also supported on Windows and is available via GitHub. See http://pmem.io
librpmem – Local node replication library
librpmemd – Remote node replication daemon

## Slide 7: PMoF Overview – NVML Overview
Want to offer HA persistent data replication to local and remote nodes
Since App-Direct memory mapping loads and stores are handled directly by the CPU, there is no way to hook these calls for replication

## Slide 8: PMoF Overview – NVML PMoF Implementation Overview
Local Node replication:
  Hook local “Make Persistent” call
  Memcopy the data being made persistent in to second local location
  Issue local CLFLUSHOPTs and PCOMMIT for each new buffer
Remote Node replication (this is example of General Server Durability Mechanism):
  Hook “Make Persistent” call
  Issue RDMA Write to push local data to the remote node
  Issue RDMA Send with a list of data to make persistent
  Remote node issues CLFLUSHOPTs and PCOMMIT
NVML local and remote replication support with existing NVML API – NO Application API Changes required for local or remote replication
Local Node
Remote Node
Out-of-band connection setup and resource exchange
CPU Flush & PCommit
Load Store
librpmemd
librpmem

## Slide 9: PMoF Overview – NVML PMoF Implementation Overview

## Slide 10: PMoF Overview – Basic Linux PMoF NVML Based Application RDMA Stack
PMoF Fabric Support utilizing libfabric
libfabric API – Common Ring3 Application interface for Ethernet (IB, RoCE, iWARP) RNICs and Omnipath
HCAs
verbs provider – libfabrics RoCE, IB and iWarp provider interface to libibverbs

## Slide 11: PMoF Overview – Basic Linux PMoF NVML Based Application RDMA Stack w Omnipath
PMoF Omnipath Support utilizing libfabric
Initial PMoF implementation utilizes kernel IO path for Omnipath support of RDMA
Future implementations will provide a native PMoF Omnipath solution that does not utilize the kernel path or RDMA Verbs

## Slide 12: PMoF Overview – NVML PMoF Implementation Details
PMoF NVML Architecture:
Utilizes libfabric and libibverbs OFA libraries
Utilizes SSL for out-of-band secure socket connection
  Setup remote files based on platform configuration file
  Exchange RKEYs
  Exchange remote node HW configuration

## Slide 13: PMoF Overview – NVML PMoF Implementation Details
Typical NVML Replication Sequence:
  Local node Application: Stores a number of cache lines
  Local node Application: Calls pmem_persist
  Local node NVML: CLFLUSHOPT(s) / SFENCE
  Local node NVML: Calls pmem_remote_persist
  Local node NVML: RDMA Write to target node RDMA Read 4B to target node Wait for RDMA Read completion Return execution to Application

## Slide 14: PMoF Overview – NVML PMoF Implementation Details

## Slide 15: PMoF – The Solution - Storage Mode Use Cases compared with existing remote replication storage use cases
TCP/IP stack
APP
PCIe
DRAM
TCP/IP stack
PCIe
DRAM
Storage stack
PCIe
NIC
NIC
NVMe
SSD
Client Node
Server Node
TCP/IP based replication to SSD
APP
PCIe
DRAM
PCIe
DRAM
Storage stack
PCIe
RNIC
RNIC
NVMe
SSD
Client Node
Server Node
RDMA based replication to SSD
NVMe xlat
APP
PCIe
DRAM
PCIe
DRAM
Storage stack
PCIe
RNIC
RNIC
NVMe
SSD
Client Node
Server Node
NVMEoF RDMA based replication to SSD
APP
PCIe
DRAM
PCIe
NVDIMM
RNIC
RNIC
Client Node
Server Node
PMoF RDMA based replication to NVDIMM

## Slide 16: PMoF – The Solution - Storage Mode Use Cases compared with existing remote replication storage use cases
Chart: Avg. 4KB Write I/O Round Trip Time Comparison NVMe+NAND SSD vs. NVMe+3DXP SSD vs. NVMeoF+3DXP SSD+SPDK vs. PMoF
| Replication to NAND NVMe SSD using DRBD | Replication to 3DXP NVMe SSD using DRBD | PMoF in General Purpose System Mode | PMoF in Appliance Mode
 | 149 | 134 | 8.721 | 4.75
NVMeoF + 3DXP NVMe SSD + SPDK

## Slide 17: PMoF – PMoF 1.0 – “General Purpose Method” – Real HW & SW
PMoF 1.0 for current platforms
General Purpose Method
-Utilizes DDIO on Target System to place incoming RDMA Write data in to LLC -RDMA Send with list of cache lines to flush
-Target SW Interrupted and CPU issues CLFLUSHOPT or each cache line written followed by SFENCE
-Target SW sends RDMA Send back to ack the Initiator SW of completion
Initiator SW
Initiator RNIC
Target RNIC
Target Memory Controller
RDMA Write
RDMA Write
Posted Write (DDIO)
RDMA Write
RDMA Write
Posted Write (DDIO)
Write data to remote PMEM
RDMA Send
RDMA Send
RDMA Send
Send
Force Write Durability
Send
Target CPU LLC Cache
PMEM
Write
Write
Target SW
CLFLUSHOPT
Write
Write
CLFLUSHOPT
RDMA Send

## Slide 18: PMoF – PMoF 1.0 – “General Purpose Method” – Real HW & SW – Latency Performance
Chart: Average unloaded replication latency using PMoF for various NICs and data sizes
| 16 | 64 | 256 | 1024 | 4096 | 16384 | 65536
Mellanox CX-4 / 40 GbE / RoCE v2 | 5.77 | 5.703 | 5.772 | 5.789 | 8.721 | 17.782 | 38.833
Chelsio T580 / 40 GbE / iWarp | 9.764 | 10.623 | 10.216 | 11.379 | 16.29 | 22.474 | 44.366
Almost 50% worse latency when compared to the Appliance Method due to increased network messages and need to wake target SW to perform flushes

## Slide 19: PMoF – PMoF 1.0 – “General Purpose Method” – Real HW & SW – BW Scalability Performance
Chart: Replication Bandwidth
| 1 | 2 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60 | 64
16B / LBG | 0.0096934 | 0.017596 | 0.029203 | 0.049636 | 0.06529 | 0.078549 | 0.087433 | 0.098206 | 0.10447 | 0.080503 | 0.082794 | 0.099397 | 0.097306 | 0.091056 | 0.095646 | 0.091073 | 0.090322 | 0.097839
64B / LBG | 0.027343 | 0.049152 | 0.11018 | 0.19239 | 0.25521 | 0.29568 | 0.33977 | 0.38477 | 0.39531 | 0.39329 | 0.37995 | 0.33742 | 0.33187 | 0.39771 | 0.36886 | 0.35 | 0.37458 | 0.39645
16B / Mellanox CX4 | 0.022548 | 0.03469 | 0.061445 | 0.067911 | 0.066147 | 0.066038 | 0.066114 | 0.065975 | 0.066096 | 0.068255 | 0.065683 | 0.067383 | 0.068472 | 0.068533 | 0.068324 | 0.068412 | 0.066735 | 0.06656
64B / Mellanox CX4 | 0.090896 | 0.13526 | 0.23935 | 0.27234 | 0.26692 | 0.26509 | 0.26728 | 0.26378 | 0.26393 | 0.26974 | 0.26868 | 0.26386 | 0.2765 | 0.26495 | 0.27218 | 0.27344 | 0.26992 | 0.27548
1KB / Mellanox CX4 | 1.4244 | 2.1888 | 3.6899 | 4.2477 | 4.2728 | 4.1842 | 4.2378 | 4.2248 | 4.3374 | 4.435 | 4.3671 | 4.3881 | 4.2951 | 4.4958 | 4.4124 | 4.3019 | 4.3913 | 4.2867
4KB / Mellanox CX4 | 3.804 | 7.9952 | 12.6087 | 17.5435 | 17.5404 | 17.2798 | 17.4414 | 17.3153 | 17.9775 | 18.1025 | 17.3247 | 17.9951 | 18.0374 | 18.031 | 17.4769 | 18.1159 | 17.6708 | 18.0478
16 KB / Mellanox CX4 | 7.2415 | 14.3488 | 23.2201 | 36.7953 | 37.0861 | 38.428 | 38.4996 | 38.4956 | 38.4626 | 38.5012 | 38.1961 | 38.2535 | 38.2781 | 38.4591 | 38.4335 | 38.2106 | 38.3946 | 38.3869
16B / Chelsio T580 | 0.0064299 | 0.033672 | 0.055562 | 0.091449 | 0.088263 | 0.084846 | 0.086557 | 0.092192 | 0.09496 | 0.095244 | 0.093916 | 0.096397 | 0.094684 | 0.09641 | 0.097004 | 0.098598 | 0.097837 | 0.09682
64B / Chelsio T580 | 0.031275 | 0.12291 | 0.22867 | 0.37446 | 0.36638 | 0.34575 | 0.35923 | 0.36076 | 0.37328 | 0.38148 | 0.3856 | 0.39434 | 0.38229 | 0.3868 | 0.39151 | 0.39322 | 0.39104 | 0.39329
1KB / Chelsio T580 | 0.26871 | 1.0359 | 2.8661 | 5.4228 | 5.0905 | 4.8476 | 5.1627 | 4.8297 | 5.4767 | 5.3426 | 5.5082 | 5.7777 | 5.9575 | 5.6951 | 6.2782 | 6.2324 | 5.7618 | 6.0452
4KB / Chelsio T580 | 0.8756 | 1.6673 | 4.871 | 17.097 | 17.3917 | 15.5858 | 16.8736 | 19.7504 | 20.8924 | 17.8348 | 21.2932 | 22.291 | 20.4416 | 23.221 | 23.9564 | 22.6307 | 22.953 | 23.3183
16 KB / Chelsio T580 | 2.9802 | 5.5584 | 19.7765 | 37.0047 | 34.3115 | 35.0026 | 35.566 | 36.4739 | 36.8127 | 37.5001 | 37.6751 | 37.8128 | 37.6355 | 38.1228 | 38.1444 | 38.2763 | 37.8156 | 38.176
At 4K Write no matter how many parallel threads we add, we can no-longer saturate the network link of 40 GigE NOTE: When compared to the Appliance Method the scalability is much worse due to increased network messages and need to wake target SW to perform flushes

## Slide 20: PMoF – PMoF 1.0 – “Appliance Method” – Real HW & SW
PMoF 1.0 for current platforms
-Requires no HW changes, no driver changes, no changes to existing RDMA protocol
-Solutions based on upper layer protocol (ULP) SW sequences easily implemented in PMEM aware applications utilizing RDMA including NVML
Appliance Method
-Utilizes Non-Allocating Writes on Target System to bypass LLC -Small RDMA Read forces Write data ahead to PMEM
Initiator SW
Initiator RNIC
Target RNIC
Target Memory Controller
RDMA Write
RDMA Write
Posted Write (Non-Allocating)
RDMA Write
RDMA Write
Posted Write (Non-Allocating)
Write data to remote PMEM
RDMA Read
RDMA Read
Read ACK
RDMA Read ACK
RDMA Read ACK
Force Write Durability
Flushing Read
PMEM
Write
Write
Read
Read Data

## Slide 21: PMoF – PMoF 1.0 – “Appliance Method” – Real HW & SW – Latency Performance
Chart: Average unloaded replication latency using PMoF for various NICs and data sizes
| 16 | 64 | 256 | 1024 | 4096 | 16384 | 65536
Mellanox CX-4 / 40 GbE / RoCE v2 | 1.952 | 1.983 | 2.476 | 2.922 | 4.75 | 11.069 | 28.743
Chelsio T580 / 40 GbE / iWarp | 5.547 | 12.831 | 6.359 | 6.958 | 9.234 | 13.923 | 29.48
Almost 50% lower latency when compared to the General Purpose Method due to reduced messages and no need to wake target SW

## Slide 22: PMoF – PMoF 1.0 – “Appliance Method” – Real HW & SW – BW Scalability Performance
Chart: Replication Bandwidth
| 1 | 2 | 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32 | 36 | 40 | 44 | 48 | 52 | 56 | 60 | 64
16B / LBG | 0.013931 | 0.027138 | 0.053347 | 0.097388 | 0.13184 | 0.14209 | 0.19699 | 0.22906 | 0.23407 | 0.24397 | 0.2184 | 0.21513 | 0.22991 | 0.22584 | 0.23177 | 0.2321 | 0.23348 | 0.2334
64B / LBG | 0.033021 | 0.061785 | 0.12668 | 0.31978 | 0.46822 | 0.5139 | 0.68381 | 0.87183 | 0.94779 | 0.94378 | 0.81857 | 0.83141 | 0.87414 | 0.88313 | 0.87478 | 0.87894 | 0.91773 | 0.92019
16B / Mellanox CX4 | 0.066593 | 0.11738 | 0.21438 | 0.39551 | 0.53782 | 0.59865 | 0.83345 | 0.97789 | 1.0749 | 1.2068 | 1.0911 | 0.99202 | 0.98627 | 1.0769 | 1.0089 | 0.98392 | 1.017 | 0.87298
64B / Mellanox CX4 | 0.26204 | 0.46313 | 0.85595 | 1.5349 | 2.2737 | 2.8791 | 3.3596 | 3.9787 | 4.4703 | 4.7755 | 4.0187 | 4.0523 | 4.0576 | 4.1908 | 3.7467 | 3.8561 | 3.9001 | 3.7137
1KB / Mellanox CX4 | 2.8564 | 4.9492 | 9.1723 | 16.845 | 23.8797 | 28.8699 | 31.303 | 32.1336 | 32.3194 | 32.4182 | 30.4382 | 30.9361 | 31.5413 | 31.0122 | 31.9966 | 32.0469 | 32.0301 | 31.7674
4KB / Mellanox CX4 | 6.9171 | 11.9079 | 21.1404 | 36.0036 | 37.6184 | 37.7202 | 37.521 | 37.4752 | 37.6405 | 37.5531 | 37.2111 | 37.3952 | 37.4845 | 37.3127 | 37.5109 | 37.3981 | 37.3913 | 37.4384
16 KB / Mellanox CX4 | 11.6663 | 24.0959 | 38.7388 | 38.7381 | 37.7753 | 35.6658 | 37.5971 | 37.8999 | 38.216 | 38.011 | 37.7334 | 37.9556 | 37.9149 | 38.0115 | 37.9058 | 38.114 | 38.4152 | 38.2525
16B / Chelsio T580 | 0.023703 | 0.046658 | 0.091307 | 0.074929 | 0.10399 | 0.17674 | 0.20694 | 0.19239 | 0.19955 | 0.22805 | 0.1969 | 0.20385 | 0.21734 | 0.20473 | 0.20632 | 0.18937 | 0.19575 | 0.19399
64B / Chelsio T580 | 0.053131 | 0.16669 | 0.33475 | 0.62868 | 0.8867 | 0.76341 | 0.92043 | 0.92066 | 0.92225 | 0.92324 | 0.82518 | 0.7672 | 0.92255 | 0.84558 | 0.81779 | 0.83862 | 0.74231 | 0.82488
1KB / Chelsio T580 | 1.1956 | 2.3499 | 4.5434 | 8.5208 | 11.9813 | 11.9966 | 14.8747 | 14.9025 | 11.2148 | 11.6469 | 12.6836 | 12.8755 | 13.0486 | 13.9471 | 11.9747 | 13.4259 | 11.6946 | 12.6917
4KB / Chelsio T580 | 3.5447 | 7.0219 | 13.417 | 25.0203 | 34.8932 | 35.8316 | 36.0272 | 36.1008 | 36.1079 | 36.0447 | 36.0132 | 36.1493 | 36.155 | 36.1216 | 36.0916 | 36.1323 | 35.5697 | 35.6791
16 KB / Chelsio T580 | 9.1081 | 17.8265 | 35.977 | 38.1123 | 38.1467 | 38.1685 | 38.1716 | 38.2045 | 38.2115 | 38.2112 | 38.283 | 38.2775 | 38.249 | 38.2747 | 38.2708 | 38.2792 | 38.1726 | 38.1565
At 1K Write no matter how many parallel threads we add, we can no-longer saturate the network link of 40 GigE NOTE: When compared to the General Purpose Method the scalability is much improved due to reduced messages and no need to wake target SW

## Slide 23: PMoF – PMoF 1.0 - Tail of the Log Use Case
Tail or the Log Use Case
-Common operation for existing DB
-Flow:
1) SW writes new entry at the end of the log 2) SW updates End of Log pointer
-Step 1 must be replicated before step 2
-Step 1 new entry must reach durability domain before end of the log pointer is changed in step 2
-Only replication of step 2 must be acknowledged
-4 RDMA messages from Initiator to Target
-2 RDMA messages from Target to Initiator
Initiator SW
RNIC
RNIC
Target Memory Controller
RDMA Write
RDMA Write
Posted Write
RDMA Read
RDMA Read
Read
Read ACK
RDMA Read ACK
RDMA Read ACK
Replicate new log entry
RDMA Write
RDMA Write
Posted Write
RDMA Read
RDMA Read
Read ACK
RDMA Read ACK
RDMA Read ACK
Replicate End of Log pointer
Read

## Slide 24: PMoF – PMoF in the Future - Tail of the Log Use Case – Future Fabric Implementations
Utilize new proposed Flush to force previous writes on the connection to be made durable before the flush is completed
Follow the Flush with a proposed Non-Posted Write operation which is a synchronous write all the way to the media.
Suggested here that the NP Write completion is not waited for but that is ope to debate. Typically the Tail of the Log use case does not need to wait for the NP Write completion.
-3 RDMA messages from Initiator to Target
-1 or optionally 2 RDMA messages from Target to Initiator
Target PMEM
Write
PCIe Wrt
Asynch Mem Wrt
Flush
PCIe Flushing Rd
Flushing Rd Rsp
NP Write
NP PCIe Wrt
Synch Mem Wrt
Flush Response
NP PCIe Write Ack
Initiator SW
Write
Flush
Replicate new log entry
Replicate End of Log pointer
RNIC
RNIC
Target Memory Controller
NP Write
Flush Response
NP Write Ack
NP Write Ack

## Slide 25: PMoF – PMoF in the Future - Tail of the Log Use Case – Future Fabric Implementations
Combine the Flush and NP Write in to a single Write w Commit instruction to improve transport efficiency
-1 RDMA message from Initiator to Target
-1 RDMA message from Target to Initiator
Target PMEM
PCIe Wrt
Asynch Mem Wrt
Write w Commit
PCIe Flushing Rd
Flushing Rd Rsp
NP PCIe Wrt
Synch Mem Wrt
Write w Commit Response
NP PCIe Write Ack
Initiator SW
Write w Commit
Replicate new log entry
Replicate End of Log pointer
RNIC
RNIC
Target Memory Controller
Write w Commit Response

## Slide 26: PMoF Overview – NVML PMoF Performance Details
pmemobj_tx_begin - start transaction
pmemobj_tx_zalloc] - allocate dictionary entry
pmem_persist, offset=4196416, length=64
rpmem_persist, offset=4096, length=32
rpmem_persist, offset=4112, length=8
rpmem_persist, offset=3937464, length=8
rpmem_persist, offset=6312, length=8
rpmem_persist, offset=4112, length=8
pmemobj_tx_zalloc - allocate Key string
6 x rpmem_persist
pmemobj_tx_zalloc] - allocate Value string
6 x rpmem_persist
pmemobj_tx_zalloc] - allocate Redis object
6 x rpmem_persist
NVML call log for single 64-byte Redis KV INSERT
pmemobj_tx_commit] - commit object allocation
rpmem_persist, offset=4196456, length=24
rpmem_persist, offset=3931112, length=24
rpmem_persist, offset=3931240, length=24
rpmem_persist, offset=3931368, length=24
rpmem_persist, offset=3931136, length=64
rpmem_persist, offset=3931264, length=64
rpmem_persist, offset=3931392, length=64
rpmem_persist, offset=4196480, length=128
rpmem_persist, offset=6144, length=8
tx_clear_undo_log - clear undo log as part of transaction commit phase
rpmem_persist, offset=6336, length=8
rpmem_persist, offset=6328, length=8
rpmem_persist, offset=6320, length=8
rpmem_persist, offset=6312, length=8
rpmem_persist, offset=6144, length=8
pmemobj_tx_end

## Slide 27: PMoF Overview – Proposed libfabric extensions for the future
fi_getinfo
Retrieve information about each fabric endpoint for a given connection
Capabilities expanded to describe byte addressable persistent memory support for each endpoint
int fi_getinfo( int version, const char *node, const char *service, uint64_t flags, struct fi_info *hints, struct fi_info **info);
Add the following capability bit to the info flags field to describe additional capabilities of the system
The caller requests specific capabilities to be supported in the info struct and the endpoint SW will update the same info struct with the supported capabilities:
FI_PMEM
  Initiator or target node is capable of supporting byte addressable persistent memory (Pmem)
  Assumes endpoint supports read/write to pmem with optional write flags: FI_COMMIT, FI_IMMED, FI_FENCE
  Endpoints that only support read or write to pmem direction can optional set the FI_READ, FI_READ_REMOTE, or FI_WRITE, FI_WRITE_REMOTE flags with FI_PMEM to report specific direction supported.

## Slide 28: PMoF Overview – Proposed libfabric extensions for the future
fi_mr_reg
Register persistent memory data buffer addresses with the fabric controller for a specific protection domain with requested accesses and return the lkey and rkey handles that describe the registered memory
By making these part of opaque rkey, initiator SW is not burdened with understanding these attributes
int fi_mr_reg( struct fid_domain * domain,
const void * buf,
size_t len,
uint64_t access,
uint64_t offset,
uint64_t requested_key,
uint64_t flags,
struct fid_mr ** mr,
void * context);
Add the following bits to the flags field to further describe the attributes of the memory region being registered. The access requested is a combination of OR’ing these new access capabilities with existing flags:
  FI_PMEM – Memory region being registered is byte addressable persistent memory
  FI_UNCACHED - Memory region should not be backed by cache. When data is written to this region, the local cpu caches should be bypassed. Without this flag being present, the write data should be placed in cpu cache as SW will most likely access the data shortly after remote transfer is complete.

## Slide 29: PMoF Overview – Proposed libfabric extensions for the future
fi_writemsg Updates
The existing fi_writemsg API is utilized for writing to persistent memory
Proposed that RDMA protocol extensions will implement the write with commit as a new opcode on the fabric
Proposed that RDMA protocol extensions will implement the write with commit with immed as a new opcode on the fabric
static inline ssize_t fi_writemsg( struct fid_ep *ep,
const struct fi_msg_rma *msg,
uint64_t flags)
struct fi_msg_rma {
const struct iovec *msg_iov;
void **desc;
size_t iov_count;
fi_addr_t addr;
const struct fi_rma_iov *rma_iov;
size_t rma_iov_count;
void *context;
uint64_t data;
};

## Slide 30: PMoF Overview – Proposed libfabric extensions for the future
fi_writemsg Updates
The following libfabric flags are added for handling writes to persistent memory.
The flags are utilized by the target node endpoint device to precisely control steering of the write data and handling of any device specific completion handling.
Therefore these indicators should be visible in the wire protocol payload and available at the target end point: FI_COMMIT – Commit to pmem all data within scope of the command.
  Completion to the initiator occurs after all data has been committed to the durable memory domain
  Previous fi_write* messages sent to the same rkey on the same QP will also be committed to durability before the completion is signaled.
    With a non-volatile memory region (memory registered with FI_PMEM), completion indicates all write data in scope has reached durability and is power fail safe. Once durability occurs the Initiator RNIC will insert a Completion WQE on the initiators CQ to notify SW.
    With a memory region that is volatile memory (memory registered without FI_PMEM). The completion indicates all write data in scope has reached the global visibility point
FI_IMMED – Used in conjunction with FI_COMMIT
  Once all write data in scope of the write has reached the pmem durability domain issue a Completion WQE to the target CQ.
  Setting this flag without setting FI_COMMIT is considered an error.
FI_FENCE – Extend the use of this existing flag to cover fencing of writes on the target node.
  When set with FI_COMMIT, the target endpoint will guarantee that previous writes with the same RKEY will be made durable before executing this fenced write to the same RKEY.

## Slide 31: PMoF Overview – Proposed libfabric extensions for the future
fi_writemsg ordering and completion semantics with PMEM
Here are the basic rules for using the fi_write* API with persistent memory:
All existing libfabric fi_write* API can be utilized to write data to PMEM by supplying an RKEY whose memory region was registered with FI_PMEM set
fi_write, fi_writev, fi_writedata, fi_inject_write and fi_inject_writedata API that do not take a flag argument cannot request data to be committed to the persistent memory durable domain
For fi_writemsg (with FI_COMMIT set) to properly commit other write data previously sent via fi_write* API methods, all of the commands must utilize the same QP for all command submittals and must utilize the same RKEY.
There is no write data ordering guarantee for any sequence of fi_write* or fi_writemsg commands sent to different QPs or different RKEYs.
The ordering of write data associated with fi_writemsg (with FI_COMMIT set) with respect to the ordering of write data for other fi_writemsg (with FI_COMMIT set) requests is indeterminate, even when issued on the same QP and RKEY. It is possible for one to pass the other. SW must utilize the FI_FENCE with FI_COMMIT to avoid this indeterminate ordering on the same RKEY. To control write data placement ordering on the same QP but to different RKEYs, SW can continue to utilize fi_read* or fi_send* API in between fi_writemsg (with FI_COMMIT set) commands.

## Slide 32: PMoF Overview – Proposed libfabric extensions – example sequences
Libfabric pmem write sequence
without proposed extensions

## Slide 33: PMoF Overview – Proposed libfabric extensions – example sequences
Libfabric pmem write sequence
with proposed extensions

## Slide 34: PMoF Overview – Proposed libfabric extensions – example sequences
Libfabric pmem write sequence
with proposed extensions

## Slide 35: PMoF Overview – Proposed libfabric extensions – example sequences
Libfabric pmem write sequence
with proposed extensions