## Slide 1: Red Hat RDMA Integration and Testing Processes
Doug Ledford

## Slide 2: Historical Releases
Red Hat Enterprise Linux 4
  Utilized OFED for both kernel code and user space packages
  Took in all of the support present in OFED
  The version of the openib rpm was == the version of OFED we pulled into any given release
Red Hat Enterprise Linux 5
  Utilized OFED for kernel code, but went directly to upstream releases for user space code
  Did not take in all of OFED kernel code either, specifically excluded features not accepted upstream
  The version of the openib rpm was == to the version of OFED we pulled the kernel support from

## Slide 3: Current Releases
Red Hat Enterprise Linux 6 and upcoming 7
  Uses upstream kernel code.
  Uses upstream user space packages.
  Uses a new package named rdma as the base kernel configuration package. Starting with EL 6.3 and later, the version of the rdma package can be used to determine the version of the upstream kernel that we pulled the RDMA support from for the current EL kernel. For instance, in EL 6.3, the rdma package is version 3.3, so for that release the core RDMA kernel support came from the upstream version 3.3 Linus kernel. For EL 7, we also encode the release number into the rdma package version to ensure proper sorting. For instance, EL 7.0’s rdma package is currently version 7.0_3.13_rc8-3.el7

## Slide 4: Integration for current releases
We perform a full kernel RDMA stack refresh with each point release, but we weed out patches that can’t be taken due to need for other items that would break kABI in our kernels (the RDMA stack is exempt from the kABI list and has been since EL 4). The git whatchanged and git cherry-pick commands are essential for this work.
We grab whichever user space packages have updated since the last point release, and rebuilt all dependent packages even if the dependent package didn’t have it’s own source update.

## Slide 5: Testing Environment
We have a specific cluster we use to test every update.
  56GBit/s Mellanox InfiniBand switch on one fabric
  40GBit/s Intel InfiniBand switch on another fabric
  40GBit/s Mellanox Ethernet switch on another fabric
  10GBit/s Dell Ethernet switch on another fabric
  We test a fairly complete matrix of all possible combinations of InfiniBand, iWARP, RoCE/IBoE, P_Keys, VLANs, and SRIOV. And across this matrix we run high level tests (such as MPI tests) as well as low level tests (simple pings run overnight in a loop) and performance oriented tests.

## Slide 6: Testing Environment (cont.)
We test across a wide array of host adapters
  mthca, mlx4, mlx5, qib, cxgb3, cxgb4, ocrdma
  Where possible, we specifically attempt to test cross driver compatibility with each release
Testing is mostly automated
  We have an install environment that installs the latest release, installs our internal test harness, then runs a complete set of automated tests across the appropriate subset of machines for each test type. Failures are flagged for further analysis.

## Slide 7: Questions?
No? Awesome, I must have explained everything perfectly! 