## Slide 1: OpenFabrics Interface WG A brief introduction
Paul Grun – co chair OFI WG
Cray, Inc.

## Slide 2
OFI WG – a brief overview and status report
Keep everybody on the same page, and
An example of a possible model for the OFA going forward (more on this later)

## Slide 3: Agenda
OFI WG
A new framework
Guiding principles
Current status, process, participation
Key issues

## Slide 4: OpenFabrics Interface WG
Last August, the OpenFabrics Alliance undertook an effort to review the current paradigm for high performance I/O.
The existing paradigm is the Verbs API running over an RDMA network.
The OFA chartered a new working group, the OpenFabrics Interface Working Group (OFI WG) to:
  Develop, test, and distribute:
    Extensible, open source interfaces aligned with application demands for high-performance fabric services.
    An extensible, open source framework that provides access to high-performance fabric interfaces and services.

## Slide 5: Put simply…
A series of “API-lets”
  vs “one API to rule them all”
A framework to support them

## Slide 6: OFI Objectives
Maximize application I/O (aka network) effectiveness
Excellent support for a wide range of (classes of) applications
Minimize interface complexity and overhead
Make the interface(s) extensible
Not constrained to a particular wire, fabric or vendor

## Slide 7: Verbs-based framework
Device(s)
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocols
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
libibverbs - 60 function calls
a series of kernel services
Support for several fabrics
adaptation layer
Support for applications

## Slide 8: Verbs-based framework
Device(s)
Hardware
Specific Driver
Connection Manager
MAD
Kernel verbs
SA Client
Connection
Manager
Connection Manager
Abstraction (CMA)
Open SM
Diag
Tools
Hardware
Provider
Mid-Layer
User verbs
User APIs
SDP
IPoIB
SRP
iSER
RDS
Upper Layer Protocols
NFS-RDMA
RPC
Cluster
File Sys
Application Level
SMA
Clustered
DB Access
Sockets
Based Access
Various
MPIs
Access to
File
Systems
Block
Storage
Access
IP Based
App
Access
Support for several fabrics
Support for applications
The OpenSource Zone
Preserve s/w investment above
Enable differentiation below

## Slide 9: Verbs API
The Verbs API closely parallels the Verbs semantics defined in the IB Architecture specs
The IB spec defines a very specific set of I/O services – RC, RD, UC…
Basic abstraction exported to an application is a queue pair
A queue pair is configured to provide an operation (send/receive, write/read, atomics…) over one of a set of services (reliable, unreliable…)
Low level details (e.g. connection management, memory management) are exposed to the application layer (which often doesn’t care about such details)

## Slide 10: Verbs model
RDMA service provider
IB
Enet
IP/Enet
Reliable service
Unreliable service
remote memory access
unicast msg service
multicast msg service
atomic operation service
QP
one API (verbs)
One service provider offering multiple services
three wire protocols
QP is a h/w construct representing an I/O port
app
API
Characteristics of the QP ‘bleed through’ to the app
QP abstracts the complete set of services, whether they are needed or not
Notes: This is the notion of “heavyweight verbs”.
Note that there is no collectives service.

## Slide 11: Observations
A single API cannot meet all requirements and still be usable
A single app would only need a subset of a single API
Extensions will still be required
  There is no correct API!
We need more than an updated API – we need an updated infrastructure
From Sean Hefty’s original proposal

## Slide 12: Streamlining the API
Provide a richer set of services, better tuned to application requirements
Broaden the number of APIs (“API-lets”), but streamline each by reducing the functions associated with it.
Each API represents a specific I/O service
APIs are composable, and can be combined
Abstract the low level fabric details visible to the application

## Slide 13: OFI Model
Fabric interface
i/f
Fabric service
Reliable service
IB
Enet
IP/Enet
Unreliable service
remote memory access
unicast msg service
multicast msg service
atomic ops
APIs expose the underlying I/O service
Multiple service providers.
Innovation in I/O service optimization occurs here.
wire protocols
i/f
i/f
i/f
…

## Slide 14: A framework
Fabric Interfaces
I/F
I/F
I/F
I/F
I/O Service Provider Layer
I/O service
I/O service
I/O service
Framework defines multiple interfaces
Implementations are optimized at the provider layer
The framework exports a number of I/O services (e.g. message passing service, large block transfer service, collectives offload service, atomics service…) via a series of defined interfaces.
* Important point! The framework does not define the fabric.
…
Notes: Solution Space – provide a framework allowing applications to select the appropriate I/O service(s), and allowing vendors to select which I/O services to implement.

## Slide 15: (Scalable) Fabric Interfaces
Q: What is implied by incorporating interface sets under a single framework?
  Objects exist that are usable between the interfaces
    Isolated interfaces turn the framework into a complex dlopen
  Interfaces are composable
    May be used together
Fabric Interfaces
Message Queue
Control
Interface
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services

## Slide 16: Guiding principles
There are really two –
Application-centric I/O
Fabric independence

## Slide 17: Application as driver
Hardware Layer
Application Interface
Application layer
Provider Layer
Examine the classes of applications that are important to target users of OFS.
Let the applications drive the appropriate interface definition.
This, in turn, drives the necessary features that the fabric should support.
Different classes of applications may require different types of I/O services
Notes: Solution Space – apply the principles of Application-centric I/O rigorously.
An Example: an MPI application may require the provider layer to provide a collectives service.

## Slide 18: A word about “applications
RDMA protocols
Transport
s/w xport interface
Network
Link
Phy
Software Transport Interface
RDMA Protocols
Network Transport Service
Let’s agree that an “application” is anything that consumes network services.
Session
Transport
App

## Slide 19: For example
IP-based,
Sockets-based apps
Support for various types of legacy apps
Various
MPIs, PGAS…
Distributed computing via message passing
Block
Storage
Network-attached block storage
Clustered
DB Access
Extracting value from structured data
File
Systems
Network-attached file or object storage

## Slide 20: Wire independence
IP-based apps
Sockets-based apps
Various
MPIs, PGAS…
Clustered
DB Access
Storage &
Data Access
Fabric interface
Good progress here
Now looking at mappings here
RNIC
HCA
NIC
???
I/O Service Provider
. . .

## Slide 21: Four activities
libfabrics
Fabric Interfaces
Fabric Provider Implementation
I/O service
I/O service
I/O service
…
Application(s)
Message Queue
Control
Interface
RDMA
Atomics
Active Messaging
Tag Matching
Collective Operations
CM Services
APIs (driven by OFA ‘interest groups’)
Application requirements
Service providers (standards driven)

## Slide 22: Some issues
Memory registration – API or provider layer?
Collectives operations
Completions

## Slide 23: OFI WG Process
Weekly telecons – Tuesdays at 9:00am PDT
All are welcome to participate
Group has well-defined processes to ensure progress
F-2-F meeting tonight following the OFA General Membership meeting

## Slide 24: Thank You