## Slide 1: NVM as a Disruptive Technology
#OFADevWorkshop

## Slide 2: Non-Volatile Memory Vision
NVM Brings Storage
To Memory Slots
NVM
Fast Like Memory
Durable
Like Storage
Make Data Durable Without Doing IO!

## Slide 3: Next Generation Scalable NVM
Family | Defining Switching Characteristics
Phase Change Memory | Energy (heat) converts material between crystalline (conductive) and amorphous (resistive) phases
Magnetic Tunnel Junction (MTJ) | Switching of magnetic resistive layer by spin-polarized electrons
Electrochemical Cells (ECM) | Formation / dissolution of “nano-bridge” by electrochemistry
Binary Oxide Filament Cells | Reversible filament formation by Oxidation-Reduction
Interfacial Switching | Oxygen vacancy drift diffusion induced barrier modulation
Scalable Resistive Memory Element
Resistive RAM NVM Options
Cross Point Array in Backend Layers
Wordlines
Bitlines
Memory
Element
Selector
Device
~ 1000x speed-up over NAND.
From Jim Pappas, Intel, SNIA NVM Summit
Notes: There is a fundamental technology transition approaching where NAND will be replaced by Resistive NVM. There are over a dozen competing technologies, and our work in the SNIA TWG is agnostic to which of those will succeed. Instead, we are focused on the common attribute that they share… that they are approaching a 1000X performance improvement in latency over NAND.

## Slide 4: Merging Storage and Memory
From Ed Grochowski, 2014 Report on New Storage Technologies
4

## Slide 5: Storage Latency is Changing
SSD Latency Profile – In the next generation, media is not the bottleneck.
From Jim Pappas, Intel, SNIA NVM Summit
Notes: The 3 bars above show advancements that the industry has been able to make with NAND based SSDs with improvements to the NAND interface (ONFI) and the SSD bus interface (PCI Express). Everything in blue (the first 3 segments) is basic latency of the NAND SSD. If this was a HDD, then the blue segments would be about 1KM long on this screen.

## Slide 6: Interconnect and Software Will Soon Dominate Latency
From Jim Pappas, Intel, SNIA NVM Summit
Notes: For clarity, let’s expand the bottom line which now clearly identifies the new system bottlenecks as the media becomes faster. The media itself becomes “insignificant”, but the bus interface and the system storage software dominate the performance.

## Slide 7: Opportunities with Next Generation NVM
NVMe & STA
SNIA
  NVM Express/SCSI Express: Optimized storage interconnect & driver
  SNIA NVM Programming TWG: Optimized system & application software
From Jim Pappas, Intel, SNIA NVM Summit
Notes: For clarity, let’s expand the bottom line which now clearly identifies the new system bottlenecks as the media becomes faster. The media itself becomes “insignificant”, but the bus interface and the system storage software dominate the performance.

## Slide 8: Application View of IO Elimination
Non-Blocking
Chart: Latency Budgets
| SATA SSD | NVMe Flash | Persistent Memory
Device | 160000 | 25000 | 50
NUMA
Software overheads are being driven to keep pace with devices
NUMA latencies up to 200 nS have historically been tolerated
Anything above 2-3 uS will probably need to context switch
Latencies below these thresholds cause disruption

## Slide 9: Memory Disaggregation
Server
Server
Server
Server
Shared Memory
Memory
Memory
Memory
Controller
Memory Semantic Fabric
Increased flexibility to provision memory from a shared pool
Pass data or VM’s between servers without moving bits
Enabled at rack scale using silicon photonics

## Slide 10: Application View of Memory Properties
Durability
Applications should know which memory is persistent.
NUMA
What part of the system manages proximity of processing to memory?
How much unpredictability is tolerable?
Multi-processing
SMP boundaries implied by distance and fault domains

## Slide 11: Abstractions need to account for…
Resource Diversity
Choosing the right memory resources in real time
System Scalability
Programming model accounts for wide scale
Transactions
Accelerate recoverability to memory speed

## Slide 12: Thriving in Chaos
Make sure hierarchy levels earn their places
Think dual stack
Make middleware take up the slack
Mind the fault lines

## Slide 13: Thank You