## Slide 1: RoCEv2 Update from the IBTA
#OFADevWorkshop

## Slide 2: Introduction – RoCE (v1)
OFA Verbs Interface
IB
Transport
Protocol
Network Layer
InfiniBand
Link Layer
InfiniBand
OFA* Stack
InfiniBand
Management
RDMA Application / ULP
Introduction - The RoCE (v1) Protocol Stack
RoCE
Ethernet
Link Layer
Ethernet
Management
IB
Transport
Protocol
Network Layer
RoCE
Specification

## Slide 3: The RoCE(v1) Packet Format
LRH
(L2 Hdr)
IB Payload
L3 Hdr
VCRC
ICRC
BTH+
(L4 Hdr)
IB Payload
ICRC
BTH+
(L4 Hdr)
FCS
Eth L2
Header
InfiniBand
RoCE
L3 Hdr
No Changes

## Slide 4: RoCE(v1) Timeline
May 2009 - IBTA forms RoCE WG
July 2009 – RoCE Prototype Available
Aug 2009 – Position paper on RoCE at HOTI
April 2010 - Ratified IBTA Standard
October 2010 – RoCE in upstream Linux

## Slide 5: RoCE(v1) and L2-Datacenters
RoCE is a L2 Protocol
  (“flat”) L2 Eth Topology
    L2 Extensions are Supported
      TRILL
      Provider Networks (PB, PBB, etc)
      Virtualization Overlays
  RDMA within an Ethernet L2 Domain
    FCoE is similar
L2
L2
L2
Plain L2 or TRILL or PBB or
Virtualization Overlays
Scale up with Single Ethernet L2 Domain
(from endnode perspective)
L2
RoCE within a Single Rack

## Slide 6: The Need for (IP) Routable RoCE
A Common Class of L3 Datacenter
  Nodes within a Rack share a Ethernet L2 Domain
  TOR Device
    L2 Switch for intra-rack communication
    L3 (IP) Router for inter-rack communication
  other topologies also apply
Customer Demand
  RDMA Across Racks
    i.e. Across IP Subnets
  Focus on Data Center Networks
RoCE is Already “close” to being “IP Routable”
  RoCE Address in API is IP
  RoCE Packet Format / Wire Protocol Includes L3 Header
L2
L2
L2
L2 Domain
L2 Domain
L2 Domain

## Slide 7: RoCEv2 – A Straightforward Extension
OFA Verbs Interface
IB
Transport
Protocol
IB Network Layer
InfiniBand
Link Layer
InfiniBand
OFA* Stack
InfiniBand
Management
RDMA Application / ULP
RoCE
Ethernet
Link Layer
Ethernet / IP
Management
IB
Transport
Protocol
IB Network Layer
RoCE v2
Ethernet
Link Layer
Ethernet / IP
Management
IB
Transport
Protocol
IP
UDP
Software
Typically HW
RoCEv2
Specification
RoCE
Specification

## Slide 8: RoCEv2 - IP Routable Packet Format
IB Payload
ICRC
IB BTH+
(L4 Hdr)
FCS
Eth L2
Header
IP
Header
EtherType
ip.protocol_number
indicates that packet is UDP
Proto #
UDP dport number Indicates
that next header is IB.BTH
UDP
Header
Port #
RoCEv2
IB Payload
ICRC
IB BTH+
(L4 Hdr)
FCS
Eth L2
Header
IB GRH
EtherType indicates
that packet is RoCE
(i.e. next header is IB GRH)
RoCE
EtherType indicates
that packet is IP
(i.e. next header is IP)
EtherType

## Slide 9: RoCEv2 Highlights
Contained Change
  Clean L3 Replacement
  Strict Layering Preserved
  Generated and Consumed Below the Channel Interface (i.e. the “API”)
Transparent to Applications
  No Application Software Changes
    Current RoCE API is already IP L3 based
Transparent to Underlying Network Infrastructure
  Mainstream processing on L2 Ethernet Switches / L3 IP Routers
Additional Benefits of the RoCEv2 Approach (some examples)
  Traditional Network Management Tools Apply
  ACLs (Metering, Accounting, Firewalling)
  IGMP Snooping for optimized Multicast
  Network Monitoring Tools

## Slide 10: Status Update
IBTA SC Requested Technical Work on RoCEv2 (Nov 2013)
IBTA Invited to give Presentation at November 2013 IETF Meeting
  IBTA Starting Definition of IP Routable RoCE
  Well Received by the IETF Community
IBTA IBXoE Working Group Re-Activated to Specify RoCEv2
  Started Work in December 2013
Initial RoCEv2 Specification Draft
  Undergoing IBXoE WG Review
Next Steps

## Slide 11: Thank You