## Slide 1: KOFI
Stan Smith Intel SSG/DPD
January, 2015
Kernel OpenFabrics Interface

## Slide 2: KOFI Mission
Future proof the kernel fabric stack (ibverbs) with a fabric independent framework.
Migrate fabric I/F from device specific to higher level message passing semantics.
Streamline code paths to device functionality (reduced instruction counts).
Incorporate high performance storage interfaces.
Coexist with current fabric interfaces.
Notes: This is an attempt to explain the 3 categories on the previous slide

## Slide 3: KOFI Framework
The KOFI framework consists of at least two cooperating components:
  KOFI (API interface) a single kernel module
  KOFI Fabric Providers (>=1) kernel modules
Providers:
Conceptually, a kofi provider may be viewed as a local hardware NIC driver, though a provider is not limited by this definition.
Devices and the drivers that plug into the kofi framework are referred to as kofi fabric providers, or simply providers.

## Slide 4: KOFI Framework - API
KOFI interfaces are designed such that they are cohesive and not simply a union of disjoint interfaces. The interfaces are logically divided into two groups:
control interfaces are a common set of operations that provide access to local communication resources.
communication interfaces expose particular models of communication and fabric functionality, such as message queues, remote memory access, and atomic operations. Communication operations are associated with fabric endpoints.
Kofi applications will typically use the control interfaces to discover local capabilities and allocate necessary resources. They will then allocate and configure a communication endpoint to send and receive data, or perform other types of data transfers, with remote endpoints.

## Slide 5: KOFI Framework
KOFI API
kernel IBverbs
iWarp
InfiniBand
KOFI API
KOFI Providers
Device Drivers
Ethernet
RDS
kSocket
RoCE
New Providers
New Devices
IBverbs Provider
RDS Provider
* Red indicates new kernel components

## Slide 6
Back-up

## Slide 7: KOFI API
KOFI API exports up
fi_getinfo() fi_fabric() fi_domain() fi_endpoint() fi_cq_open() fi_ep_bind()
fi_listen() fi_accept() fi_connect() fi_send() fi_recv() fi_read() fi_write()
fi_cq_read() fi_cq_sread() fi_eq_read() fi_eq_sread() fi_close() …
KOFI API exports down
kofi_provider_register() During kofi provider module load a call to kofi_provider_register() supplies the kofi-api with a dispatch vector for fi_* calls.
kofi_provider_deregister() During kofi provider module unload/cleanup kofi_provider_deregister() destroys the fi_* runtime linkage for the specific provider (ref counted).
KOFI API (extremely thin code layer)
Notes: Not sure this helps. It’s meant to suggest messages can be used for specific purposes, like at a trade show or as an element of recruiting

## Slide 8: KOFI Provider
kofi_provider_register (uint version, struct kofi_provider *provider)
kofi_provider_deregister (struct kofi_provider *provider)
struct kofi_provider {
const char *name;
uint32_t version;
int (*getinfo)(uint32_t version, const char *node,
const int service, uint64_t flags,
struct fi_info *hints, struct fi_info **info);
int (*freeinfo)(struct fi_info *info);
int (*fabric)(struct fi_fabric_attr *attr,
struct fid_fabric **fabric, void *context);
};

## Slide 9: KOFI Application Flow
KOFI initialization:
  fi_getinfo( &fi ) Acquire a list of available fabric providers.
  Select appropriate fabric (traverse provider list).
  fi_fabric(fi, &fabric) create a fabric instance based on fabric provider selection.
  fi_domain(fabric, fi, &domain) create a fabric access domain object.

## Slide 10: KOFI App. II
KOFI End Point setup:
  fi_ep_open( domain, fi, &ep ) create a communications endpoint.
  fi_cq_open( domain, attr, &CQ ) create/open a Completion Queue.
  fi_ep_bind( ep, CQ, send/recv ) bind the CQ to an endpoint
  fi_enable( ep ) Enable end-point operation (QP RTS).

## Slide 11: KOFI App. III
KOFI connection components: (not for Reliable Datagrams)
  fi_listen() listen for a connection request
  fi_bind() bind fabric address to an endpoint
  fi_accept() accept a connection request
  fi_connect() post an endpoint connection request
  fi_eq_sread() blocking read for connection events.
  fi_eq_error() retrieve connection error information

## Slide 12: KOFI App. IV
KOFI Reliable Datagram data transfer:
  fi_sendto() post a Reliable Datagram send request
  fi_recvfrom() post a Reliable Datagram receive request.
  fi_cq_sread() synchronous/blocking read CQ event.
  fi_cq_error() retrieve data transfer error information
  fi_close() close any kofi created object.

## Slide 13: KOFI App. V
KOFI buffered data transfer:
  fi_mr_reg( domain, &mr ) register a memory region
  fi_close( mr ) release a registered memory region
  fi_send( ep, buf, len, fi_mr_desc(mr), ctx ) post async send from memory request.
  fi_recv( ep, buf, len, fi_mr_desc(mr), ctx ) post async read into memory request.
  fi_sendmsg() post send using fi_msg (iovec + imm data).
  fi_readmsg() post read using fi_msg (iovec + imm data).

## Slide 14: KOFI App. VI
KOFI Reliable Datagram data transfer:
  fi_sendto() post a Reliable Datagram send request
  fi_recvfrom() post a Reliable Datagram receive request.
  fi_cq_sread() synchronous/blocking read CQ event.
  fi_cq_error() retrieve data transfer error information
  fi_close() close any kofi created object.

## Slide 15: KOFI App. VII
KOFI RDMA data transfer:
  fi_write() post RDMA write.
  fi_read() post RDMA read.
  fi_writemsg() post RDMA write (iovec).
  fi_readmsg() post RDMA read (iovec).