## Slide 1: Application Access to Persistent Memory – The State of the Nation(s)!
Stephen Bates, Paul Grun, Tom Talpey, Doug Voigt
Microsemi, Cray, Microsoft, HPE

## Slide 2: The Suspects
Stephen Bates Microsemi
Paul Grun Cray
Tom Talpey Microsoft
Doug Voigt HPE
Notes: Paul to add this

## Slide 3: We’ve Come a Long Way, Baby!
Notes: We’ve come a long way baby! Can give ourselves a slap on the back.
Leased at 3200 a month (28000 in today’s money)
About 5MB
7bit characters!!
1200 rpm
Seek ~600ms
http://www.snopes.com/photos/technology/storage.asp

## Slide 4: Persistent Memory (PM)
Low Latency
Memory Semantics
Storage Features
Notes: We want three things from PMEM.
Low latency access
memory sematic access
Storage features – persistence, DI, RAID, replacement in field etc.
If you don’t need low latency then don’t bother with PMEM (a mmap’ed SSD will do the job just fine). Maybe mention sub10us though we can cover that later.
For storage features touch on RAID, replacement of FRUs and data-integrity

## Slide 5: Taxonomy
NVM – Non-Volatile Memory. All types, including those that are not byte-addressable
PM – Persistent Memory. Sometimes PMEM is used but we use PM in this talk
NVMe – NVM Express. A block protocol to run over PCIe, RDMA or Fibre Channel. A SATA/SAS replacement.
NVMP – NVM Programming Model. Application-visible NVM behavior
NVMf – NVMe over Fabrics. NVMe extended over fabrics

## Slide 6: Low Latency
 | Latency | Relative
L1 Cache Read | 0.5ns | 1
L2 Cache Read | 7ns | 14
DRAM Read | 100ns | 200
The PM Opportunity |  | 
NVMe DRAM SSD Read | 10us | 20,000
NVMe NAND SSD Read | 150us | 300,000
SAS HDD | 500us | 1,000,000
NVMe SSDs are (relatively) high latency!
PM provides persistence at memory-like speeds and semantics
Notes: Mention NVMe is adding memory semantics
Mention that PMEM is all about persistence near (in time) to the processor. Nobody should store data in PMEM unless that plan to process it.

## Slide 7: Where Are We?

## Slide 8: What is Needed?
Media &
Form-Factors
Protocols & Inter- connect
OS Support
Libraries & Toolchain
Apps
Notes: The PMEM Jigsaw
Progress being made on each of the pieces
All the outer pieces need to be in place to deliver on the last (middle) piece

## Slide 9: Lots of Moving Parts
APIs
Drivers
Communications
Infrastructure
Non-volatile Media,
Form Factors
Media &
Form-Factors
User space apps
Kernel space apps
Communications middleware
Apps
Protocols &
Interconnect
OS Support
Libraries & Toolchain
Consumers
Infrastructure
Media,
Form Factors
Protocols &
Interconnect
Notes: It is a complex problem, with lots of moving parts

## Slide 10: Where does PM sit? (Answer – anywhere it wants to)
CPU
DRAM
PM
NAND
NAND
PM
Fabric
PM
NAND
PCIe
DDR
Notes: And to add to the complexity, we have to deal with both NAND and PM devices that can be sited anywhere.
Also mention that CPU vendors are the ones who decide what comes out of their processors.
Mention other interfaces including: NVLINK, CAPI, RAPID-IO
Under ‘fabrics’, we are describing the organizations that play a significant role in influencing the fabric implementation, not just the purveyors of the hardware.

## Slide 11: Rationalizing the Problem Space
APIs
OFI, Verbs, NVMF, ND, NDK
network
Non-volatile Media,
Form Factors
Memory
byte-addressable
Storage
object, file, block…
I/O bus
memory bus
NVM consumers
11
SNIA, OSVs …
OpenFabrics Alliance, NVMe Inc,
Linux,
Windows…
IETF, IBTA, PCIe SIG, OS drivers…
Vendors, JEDEC…
Notes: Managing complexity is what engineers do best, usually by partitioning large, sticky problems into small, manageable chunks.
ND, NDK are Windows APIs for driving fabric devices, similar to verbs

## Slide 12: Start with Consumers of NVM Services
storage client
NIC
file system
DIMM
DIMM
user app
virtual switch
POSIX read or write
load/store, memcopy…
provider
Apps
NVDIMM
NVDIMM
NVM
devices
(SSDs…)
Remote NVM device (storage, memory)
Notes: It begins by understanding who the consumers are, and what they need.
Consumers are characterized by, among other things, the way that the NVM device is accessed.
Is it accessed using some sort of block-based I/O protocol?
Is it accessed using memory semantics?
Not all NVM devices are created equal; some don’t have the latency characteristics needed to respond well as remote memory

## Slide 13: Application View
PM Aware Apps
PM Device
File APIs
Ld/St
User
Kernel
PM Aware File Systems
MMU
Mapp
ings
PM data structure libraries
Middleware features
e.g. RAID
SNIA NVMP
  Describe application visible behaviors
  APIs align with OSs
PM File System Actions
  Map – expose PM directly to applications
  Optimized Flush – make data persistent
Apps

## Slide 14: Possible Stack for NVM Access
kernel application
SSD
VFS / Block Layer
HBA
local I/O
NVMe
SCSI
local
byte
addressable
ulp
SSD
NVDIMM
byte access
PCIe
mem bus
PCIe
user app
remote
byte
addressable
byte access
kfabric
kverbs
HCA
NIC, RNIC
SRP, iSER, NVMe/F, NFSoRDMA, SMB Direct, LNET/LND,…
VFS / Block I/O / Network FS / LNET
NIC
iSCSI
remote I/O
sockets
provider
fabric-specific device
libfabric
kernel application
user app
provider
APIs
Notes: Key point: NVM services are exported to the consumer via a series of APIs. The API, in turn, defines the features that are available to the consumer.
There are several organizations involved in developing network APIs for NVM, which are by-and-large harmonious.

## Slide 15: Optimizing Fabrics for NVM
storage client
NIC
user app
NVM client
NIC
NVM server
NVM
device(s)
I/O bus
mem bus
Add persistence semantics to RDMA protocols
  Register persistent memory regions
  Completion semantics to ensure persistence, consistency
  Client control of persistence
Solve the “write-hole” problem
Lots of Initiatives underway!
Can we make this work for NVDIMMs? NVMe SSDs with CMBs?
Notes: Clearly there is lots of work to do here

## Slide 16: Simple Math
NVMe
+ RDMA
-------
AWESOME
PM
+ RDMA
--------
AWESOME2

## Slide 17: …continuing down the stack
APIs
-OFI, Verbs, NVMe/F…
network
Non-volatile Media,
Form Factors
Memory
byte-addressable
Storage
-object, file, block…
I/O bus
memory bus
NVM
consumers

## Slide 18
NVMe over Fabrics – Present an NVMe block device to a client over RDMA or Fibre Channel
NVMe Controller Memory Buffers – Standardize (persistent) PCIe memory on NVMe devices. NVDIMM-N on PCIe bus?
LightNVM – A low-level SSD interface that is more aligned to the underlying media (NAND)
Notes: Updates and current topics in the NVMe Standards body

## Slide 19: Media
Category | Vendors | Comments
DRAM Drop-In | Everspin Micron Toshiba/SK Hynix | DRAM like latency Super-Cap Replacement Not for bulk storage Memory Interface
Storage Class Memory | Micron-Intel SanDisk Toshiba Crossbar Nantero | Faster than NAND, Cheaper/Slower than DRAM Byte Addressable Block and Memory Interfaces
NAND | Micron Toshiba SanDisk SK Hynix Samsung | Lowest cost Slow (for NVM) Not byte addressable cheap and plentiful Block Interface
PM
NOT PM
NVM

## Slide 20: PM Form Factors
NVDIMM-N
NVDIMM-P
Not-NAND NVMe
NAND NVMe

## Slide 21: PM Form Factors
Form-Factor | Media | Latency | Memory Semantics | Storage Features
NVDIMM-N | DRAM/ MRAM |  |  | 
NVDIMM-P | NAND/ PM |  |  | 
Non-NAND NVMe | DRAM/ PM |  |  | 
NAND NVMe | NAND |  |  | 
Form factors impact Features
(No DMA engines on a DIMM!)
Notes: NVDIMM-P user slower media than NVDIMM-N but less overhead than NVMe.
NVDIMM-P may present memory semantics to the CPU/OS but underneath it may be using block media (NAND).
NVDIMM-N stores data as cachelines. Impossible to get good ECC and DI out of that. Also no DMA engines in a DIMM form factor.

## Slide 22: PM Scenarios
PM region as a block device (a la persistent ram disk).
Filesystems support: direct access to the memory (e.g DAX), PM aware FS (e.g. m1fs).
You can put your files, databases etc. on top.
Remember we are crawling right now!
Soon: Shared persistent memory
Notes: Note that right now this is only x86_64.
Mention that I have PMEM performance data for NVMDIMM-N in my other talk.

## Slide 23: Libraries and Toolchains
int main(int argc, char *argv)
{
printf(“Hello, PMEM World!\n”);
return 0;
}
section .text
global _start
_start:
mov edx,len
mov ecx,msg
mov ebx,1
mov eax,4
int 0x80
mov eax,1
int 0x80
section .data
msg db 'Hello, PMEM World!',0xa
len equ $ - msg
Make it easy for applications to utilize PM, regardless of OS and ARCH!
Vs
EASY
HARD
Notes: Which would the user prefer to write.
Slide showing how hard it is to code without glibc and discussing nvml.
Library support that is portable across OS and ARCH. NVML is a start.
Bindings for all common languages.
Compiler, assembler and linker support in the most popular toolchains.

## Slide 24: Call to Arms
Notes: Lots done, lots still to do
Not quite a Sisyphean task but there is a lot of work to be done

## Slide 25: Call to Arms
Libraries and Toolchains: NVML for non-x86, integration into glibc/gcc etc.
Media & Form Factors: Production PM, appropriate PM form factors.
Protocols and Interconnect: Enhancements to NVMe and RDMA, PM over Fabrics, standardization of memory channels.
OS Support: ISA updates, DAX devices, Other OS, new OSes?

## Slide 26: Conclusions
We are almost walking! Help out if you can
If you want sub 10us access to persistent data then PM may be for you
The CPU vendors have a lot of say in the interconnect but some open options exist too
Toolchains, libraries and OSes are adapting
New applications will complete the jigsaw and lead to revenue