## Slide 1: Persistent Memory over Fabrics
Rob Davis, Mellanox Technologies
Chet Douglas, Intel
Paul Grun, Cray, Inc
Tom Talpey, Microsoft

## Slide 2: Agenda
The Promise of Persistent Memory over Fabrics
  Driving new application models
How to Get There
  An Emerging Ecosystem
  Encouraging Innovation
  Describing an API
API Implementations
  Flush/commit is the way to go
  But how to optimize these operations?

## Slide 3: Persistent Memory (PM)
Persistent Memory (PM) Benefits
  Considerably faster than NAND Flash
  Performance accessible via PCIe or DDR interfaces
  Lower cost/bit than DRAM
  Significantly denser than DRAM
PM
Leading Edge PM Technologies

## Slide 4: PM Needs High Availability (HA)
 | PM | NAND
Read Latency | ~100ns | ~20,000ns
Write Latency | ~500ns | ~50,000ns

## Slide 5: Applications Enabled by PM
Compute Disaggregation
Scale out file/object systems
In-Memory Database
Machine learning
Hyperconverged Infrastructure

## Slide 6: Compute Disaggregation

## Slide 7: Core Requirements for Networked PM
PM is really fast
  Needs ultra low-latency networking
PM has very high bandwidth
  Needs ultra efficient, transport offload, high bandwidth networks
  Remote accesses must not add significant latency
PM networking requires:
  Predictability, Fairness, Very Low Packet Loss
 | PM | NAND
Read Latency | ~100ns | ~20,000ns
Write Latency | ~500ns | ~50,000ns

## Slide 8: We Can Get There
HGST live demo at FMS 2015
PM based Key-Value store over 100Gb/s fabric
Key-Value Store fetch from non-volatile memory in 5usec

## Slide 9: How to get there – the PM Ecosystem
APIs
libfabric, Verbs, NVMF, ND, NDK
Persistent Memory Media,
Form Factors
Memory
Storage
object, file, block…
network
H/W
SNIA, OSVs. Language writers, App developers, middleware providers
IBTA, OpenFabrics Alliance, NVMe Inc,
Linux, Windows…
IETF, IBTA, OS drivers, N/W Vendors…
Vendors, JEDEC…
network
H/W
network
H/W
provider
provider
provider
…
…
Today’s Focus
Notes: This slide needs to convey the overlap between OFIWG as a developer of an API and (OFA+IBTA) as a developer of the verbs API.

## Slide 10: No one argues with this…
remote storage
remote PM
local mem
latency
pS
uS
mS
Data Storage
Data Access, Data Sharing…
What happens when apps can access shared information at near-memory speeds?
How will apps evolve to take advantage of pools of global, shared, PM?
What happens when apps evolve in the ways that they access, share and consume data?
Persistent memory changes the way that applications store, access, communicate and share information
What should network architects do to prepare?
Notes: Persistent memory is (or soon will) change the landscape. We in the networking community are preparing for the ground shift.

## Slide 11: Focus on memory operations
storage client
NIC
file system
DIMM
DIMM
user or kernel app
virtual switch
POSIX I/F
load/store, memcopy…
provider
NVDIMM
NVDIMM
NVM
devices
(SSDs…)
remote storage class memory, persistent memory
Storage
- object, file, block
- storage class mem
Memory
- persistent memory
Think about accessing PM using memory paradigms, as opposed to storage paradigms…
…even if the data at the far end is stored as a memory mapped file.
Notes: Taxonomy – let’s be clear on the different access methods. For this talk today, we’re not talking about NVMe/F – we’re talking about PM

## Slide 12: Simultaneous Equations to Solve
API
user app, middleware, languages…
Consumer of network services
Fabric Independent
Different Providers for different fabrics
H/W device
Provider
H/W device
Provider
H/W device
Provider
…
Define the functions to be exported upward
Implement APIs for the fabrics of interest
Let consumers drive the requirements

## Slide 13: Representative Use Cases
NVDIMM
app
NVDIMM
Replication
High Availability use case
app
global shared memory service
NVDIMM
app
Shared PM
Remote Access, Storage use cases
app
app
app
Notes: We don’t yet know much about how PM is going to be deployed, but these two use cases are a good start

## Slide 14: How they work
mem ctrl,
library
user
store,
store,
store,
commit
Local
NVDIMM
Remote
NVDIMM
completion
user
Remote
NVDIMM
completion
High Availability Use Case
Remote Shared Memory Use Case
user
put
get
notice
write,
write,
write,
commit
store,
store,
store,
flush
Notes: Remote memory use case. Remote persistent memory appears as a fabric-attached service which is shared by number of clients.

## Slide 15: Shared PM - A Closer Look
Remote
NVDIMM
valid
user
put
put
put
commit
get
notice
persistent
node
cntlr
user
API Requirement: Distinguish between data which is globally valid, and data which has been made persistent
Notes: Remote memory use case. Remote persistent memory appears as a fabric-attached service which is shared by number of clients.

## Slide 16: The Beginnings of a List of API Reqmts
user
user
Applications Requirements – a starting point
Ability to force flushes of local caches to remote persistent memory
Perform non-cached writes to remote to persistent memory
Identify the persistence characteristics of a remote memory device
Distinguish between data which is globally valid and data which is remotely persistent
user
Notes: Remote memory use case. Remote persistent memory appears as a fabric-attached service which is shared by number of clients.

## Slide 17: Basic API Features (example)
Consumer
PUT w/ Commit
Write
Commit
ack
Completion
completion
API
Magic Happens
Plenty of work to be done to define the semantics of the API
Lots more to figure out how to implement the semantics over a given wire
persistence domain
Commit
completion
provider, fabric adapter
provider, fabric adapter
Notes: From those two use cases, there are some things we already know we’re going to need to do.

## Slide 18: Fabric Implementations
Utilize FLUSH to force previous writes on the connection to be made durable before the flush is completed
consumer
provider, fabric adapter
provider,
fabric adapter
remote
mem subsystem
remote
pmem
API
fabric
specific
platform
specific
PUT w/ Commit
PUT
Write
PCIe Wrt
Asynch Mem Wrt
Flush
PCIe Flushing Rd
Flushing Rd Rsp
NP Write
NP PCIe Wrt
Synch Mem Wrt
Flush Response
Completion
NP PCIe Write Rsp

## Slide 19: Alternate Fabric Implementation
consumer
provider, fabric adapter
provider,
fabric adapter
remote
mem subsystem
remote
pmem
API
fabric
specific
platform
specific
PUT w/ Commit
PUT
Write
PCIe Wrt
Asynch Mem Wrt
Write w/ Commit
PCIe Flushing Rd
Flushing Rd Rsp
NP PCIe Wrt
Synch Mem Wrt
Flush Response
Completion
NP PCIe Write Rsp
An alternative approach:
combine the FLUSH and following WRITE into a WRITE w/ COMMIT

## Slide 20: Fabric Implementations
Challenge to the industry is to extend the existing fabric protocols to provide:
Efficient, low overhead PMEM semantics
Simple provider fabric adapter implementation
Flexible, extensible across common fabric types

## Slide 21
Q & A, Discussion
Rob Davis, Mellanox Technologies
Chet Douglas, Intel
Paul Grun, Cray, Inc
Tom Talpey, Microsoft

## Slide 22: Thanks!