## Slide 1: Persistent memory support
Sean Hefty, OFIWG Co-Chair
August 8, 2017
Intel Corporation

## Slide 2: librpmem
Addressing
  host@hostname:port
  Uses out of band ssh connection for security
  Requires daemon be executing at peer node
Transfers from local pmem to remote pmem
Use case is high-availability
  Conceptually a file based duplication scheme
Memory-mapped usage model
  File mapped to memory address
  Use memory load/store, rather than read()/write()
For accessing remote persistent memory

## Slide 3: librpmem API
rpmem_create
  Creates a ‘file’ at target
    Named target memory region
  Also acts as open:
rpmem_open
  Opens a file stored in pmem
  Creates 1 or more connections to file
    Connections are abstractions referenced by index
  File is ‘mapped’ to given address
    Assumes local cached file of same size

## Slide 4: librpmem
rpmem_persist
  Persistent write to target memory region
  Blocks until write is committed
  Application must have written updates to local copy of file
rpmem_read
  Read from persistent target memory region
  Blocks until read completes
  Updates local copy of file with remote file

## Slide 5: libpmem
pmem_is_pmem
  Identify if an address range is backed by persistent memory
pmem_map_file
  Similar to mmap
pmem_persist
  Commits all data in specified range
  Range must refer to persistent memory
pmem_msync
  Similar to pmem_persist, but allows mixing pmem with normal memory
pmem_flush / pmem_drain
  Flush data from CPU caches to pmem and commits changes
  Combine implement pmem_persist
For accessing local persistent memory

## Slide 6: libpmem
pmem_memcpy_persist
pmem_memmove_persist
pmem_memset_persist
  Write data to persistent memory and commit
pmem_memcpy_nodrain
pmem_memmove_nodrain
pmem_memset_nodrain
  Write data to persistent memory, but defer commit (drain) step

## Slide 7: Intel CPU Instructions
CLFLUSHOPT
  void _mm_clflushopt(const void *p)
  Optimized cache-line flush instruction
  Writes dirty cache lines to memory
  Invalidates cache line
CLWB
  void _mm_clwb(const void *p)
  Cache line write back
  Writes dirty cache lines to memory
  Does NOT invalidate cache
Must specify each cache line

## Slide 8: OFI Data Transfer Options
Persistent writes
  RMA write to peer pmem MR
  Source region may be pmem or normal memory
Persistent reads
  RMA read into local pmem MR
  Peer MR (read source) may be pmem or normal memory
Atomic operations
  Allow for future extensions to support
  Do not define for now
  TBD: are current read/write operations actually atomic wrt failures?

## Slide 9: OFI Commit Semantic Options
Commit definition
  Data that targets a pmem region is considered persistent
    Region may be local (read) or remote (write)
  Completion indicates data can survive power failure
Commit granularity
  Per local endpoint (i.e. globally)
  Per peer endpoint (data flow)
  Per local/peer memory region
  Per address range (data region)
  Single operation
rpmem_write maps to single operation

## Slide 10: API Proposal – fi_getinfo
Capability bit: FI_RMA_PMEM
Indicates provider supports RMA to/from persistent memory
All RMA related attributes also apply to PMEM
  FI[_REMOTE]_READ/WRITE
  FI_ORDER_{R,W}A{R,W}
  rma_iov_limit
  max_order_{r,w}a{r,w}_size

## Slide 11: API Proposal – memory registration
Access flag: FI_RMA_PMEM
Specified region refers to persistent memory
mr_mode interactions
  FI_MR_LOCAL
  FI_MR_RAW
  FI_MR_VIRT_ADDR – assumes peer pmem has been mmapped
  FI_MR_ALLOCATED
  FI_MR_PROV_KEY – provider may need key to distinguish MR type
  FI_MR_MMU_NOTIFY – assumes mmapping
  FI_MR_RMA_EVENT – pmem + counter usage?
  FI_MR_ENDPOINT
Need to determine interactions with existing MR mode bits

## Slide 12: API Proposal – Data Transfers
Flag: FI_COMMIT_COMPLETE
Completion indicates that transfer was committed to target memory region
If target region is persistent, completion indicates data is durable
Commit must occur prior to notifying peer
  E.g. updating counter, writing CQ data
Possible first enhancement to API

## Slide 13: Possible Future API Additions
fi_write_flush()
  fi_writemsg() call with FI_FLUSH operation flag
  Target address ranges are flushed or committed
  Used to commit previous write operations
  No write data is transferred
    Peer counters are unaffected
  May transfer remote CQ data